## Slide 1: Chirinet Wireless Network
Notes: Chirint Wireless network has been in place for about 4 years.
Since the begining it has been all Karlnet Turbocell in Volcan
The 50 km link 1-5 was recently changed to a a 5.8 gHz backhaul
All other links are in 2.4 gHz, links 1-2, 2-3 and 3-4 are 802.11b and do not work well
Points 6 and 10 are Turbocell AP’s on reflashed Lucent AP1000’s

## Slide 2: What is 802.11 a/b/g
a is 5.8 gHz at 54 mb
b is 2.4 gHz at 11 mb
g is 2.4 gHz at 22 mb
what is defined in the standard
clients and ap's

## Slide 3: How Far will it go?
802.11 was designed for Wireless LOCAL area LANs.
Specification has time limits between Packet send and ACK received.
This limits RF distance.

## Slide 4: Turbocell and StarOS
What it Turbocell and StarOS
Can I really get 11 mb of data?
How much bandwidth do I need?
How far do I need to go?

## Slide 5
Power and Range
2 Mbps DSSS
250-350 feet radius@100mW
5.5 Mbps DSSS
130-150 feet
radius@ 100mW
11 Mbps DSSS
100-150 feet radius@ 100mW

## Slide 8
At 40 km
Curvature is 78 ft and
Fresenel is 72 ft
Minimun antenna hight must be 150 feet

## Slide 9
Are you legal?

## Slide 10: What equipment do I use?
My equipment is mostly old use and purchased on ebay.
Lucent AP 1000
Lucent Orinoco silver
Lucent RG 1000
YDI Amplifiers
Any antennas I can get or make
Times Microwave LMR-400
All hardware is reflashed with Karlnet Software, it is not 802.11b
I have samples of all hardware here for you to look at.

## Slide 11: What are we going to do in the workshop?
We will do some calculation
We will configure an Ah-hoc network
We will set up an local network with some AP’s
We will create a backbone between AP’s
We can visit some field sites, time permitting.

## Slide 12: My BIG Tip!
If the calculations say it will not work, don’t go to the field and try it.
If the calculations say it might work, in the field it might not work.
Questions