GEOF 271

Processing of earthquake

data

Jens Havskov

jens@geo.uib.no

Department of Earth Science

University of Bergen

Norway

September 2007

Introduction

The purpose of this course is to get a practical understanding of the most common processing techniques in earthquake seismology. The course will deal with manual methods and computer assisted methods, although most exercises are computer based.

In order to follow the course, the student must have basic seismological knowledge based on 'Modern Global Seismology', by Lay and Wallace or ‘An introduction to seismology, earthquakes and earth structure’ by Seth Steim and Michael Wysession as given in the course GEOF270. The two courses are given in parallel with the intention that the student follow both courses at the same time in order to get practical hands on experience while studying the background for the exercises. The main background material is thus covered in Lay and Wallace or Stein and Wysession, while additional material and similar material is given in these notes.

The SEISAN software is used for the computer processing and a SEISAN manual is required.

The software, including manual and training course, can be downloaded from

http://www.geo.uib.no/Seismologi/SOFTWARE/SEISAN_8.1/. The software should be installed on the student’s local PC  before starting the exercises since it will be used throughout.

A written report has to be made for each exercise and the reports count for 50 % of the course grade.

There are 10 exercises covering the topics:

1	Seismic phases and the Wadati diagram.

2	Manual earthquake location and earthquake catalogs

3	SEISAN: Seismic data in the computer: Data bases, epicenter maps and digital

waveform data

4	Picking phases and doing earthquake location by computer

5	Seismograms and response functions

6	Magnitude and b-value

7	Using a single station or array for azimuth determination and earthquake location

8	Fault plane solution

9	Spectral analysis

10   	Analysis of a set of local events

Additional material included:

Seismic phases, Kulhanec							p    43

Selected NMSOP (Bormann, 2002) notes and exercises:

Section IS 11.1	Earthquake location				p    87

Section 3.4 		Fault plane solution				p  117

Section Ex 3.2		Exercise in fault plane solution		p  131

Section Ex 3.4 	Exercise in spectral analysis			p  139

Other material

At  (http://www.geo.uib.no/Seismologi/SOFTWARE/SEISAN_8.1.2/)

SEISAN Version 8.1 – introductory training course

At http://www.geo.uib.no/seismo/REPORTS/COURSE_MATERIAL/

Bullen travel time tables

Old exams

Pensum: Mainly the result of the exercises and the material in this document.

This document found at http://www.geo.uib.no/seismo/REPORTS/COURSE_MATERIAL/

EXERCISE  1

Seismic phases and Wadati diagram

The purpose of this exercise is to become familiar with analog seismograms, identify basic seismic phases and use the Wadati diagram for checking the observations and calculate the Vp/Vs velocity ratio.

For this exercise, SEISAN program lsq can be used for least squares.

Exercise 1

Calculate Vp/Vs using travel time tables

Use the travel time table for crustal phases in Kulhanek, p53. Assume a constant velocity, calculate the corresponding Vp/Vs values for Pg/Sg, P*/S* and Pn/Sn at a 160 km's distance.

-How do they compare, explain any differences.

-Calculate the average P-velocities for the 3 types of phases at160 km epicentral distance.

-Plot the  travel time curves and calculate the true Pn and P* velocities from the slope of the  curve.

-Explain the differences with the average velocities.

Exercise 2

Read local seismic phases and make a Wadati diagram (see Appendix 2, IS 11.1)

Figure 1.1 shows a seismogram with traces of some stations. Read the P and S-arrival times for all stations, assume all to be first arrivals (just P and S).

-Make a table of the readings.

-Make a Wadati diagram to determine if the readings are reasonable. Put station names on the plot.

-One of the stations probably has a timing problem (on the plot, the point representing the station is off the line). Which station ? How much is the error ?

-Determine Vp/Vs, is it reasonable ?

-Determine the origin time (measuring on graph is easiest, program lsq can also be used).

Exercise 3

Read global seismic phases

Figures 1.2 and 1.3  show LP Z seismograms for 2 different events. The goal of the exercise is to determine as many phases as possible using the Bullen tables and/or travel-time figures. One event is shallow and one is deep. Some idea of the depth might be obtained by comparing the surface waves, since a shallow event will have larger amplitude surface wave relative to P and S waves than a deep event.

-For the shallow event, identify prominent phases on the seismograms and transfer the arrival times to a strip of paper which has the same time scale as one of the figures of the travel time curves (Figure 1.4, figure in Bullen, also found in text books). Slide the strip of paper to different distances in order to fit as many phases as possible, see Figure 1.5. Once the best fit is obtained, write the names of the identified phases on the seismograms.

Put results in a table and calculate arrival time relative to P. How well do the phases fit ?

- For the deep one event, identify the pP phase (assuming it to be the first phases after P) and find the depth (assume a distance of 51 degrees). The identify other phases using the Bullen tables or TTIM program.

-Determine the origin time for both events and epicentral distance for the shallow event using the Bullen travel time table or the travel time curve.

Exercise 4

Calculate travel times with a program

The program TTIM in SEISAN calculates travel times using the IASP91 traveltime tables. These calculations should be more accurate than the Bullen travel times. Note that the program uses distance in degrees, not km. One degree is 111.1 km.

-Compare the traveltimes for at least 5 different phases identified above as calculated with the Bullen tables and the IASP91 tables (the TTIM program). Use the approximate distance calculated above

-What is the % difference in travel times.

Use the Kulhanec (p 53) travel time table for Sweden and read travel times at 250 km distance.

-Make a table with the crustal phases Pg, Pn and Pb(P*), Sg, Sn and Sb. Compare travel times to IASP91 times and give difference in % of travel times.

-Which crust is the fastest, IASP91 or Sweden

Figure 1  A seismogram of a local earthquake in Western Norway. The numbers above the traces to the right is the maximum count and the numbers to the left are the DC values (counts). The time scale on the printed page is 3 mm/s.

Figure 1.2  LP seismogram. The figure shows the seismogram of distant earthquake recorded on the WWSSN photographic system. The gain is 1500. The hand written numbers are hour marks and there is one minute between dots. The time scale on the printed page is 10 mm/min.

Figure 1.3 LP seismogram. The figure shows a LP seismogram of a distant earthquake. The distance between the dots is one minute. The time scale on the printed page is 5 mm/min.

Figure 1.4  Global travel time curves for a shallow source (zero depth)

Figure 1.5  Identification of seismic phases using the strip method. Note that the time axis is on horizontal axis in contrast to Figure 1.4.  Figure from Payo (1986).

EXERCISE  2

Manual earthquake location and earthquake catalogs

In this exercise, the purpose is to get familiar with the most basic earthquake parameters, the earthquake location. The first exercise deals with manual location of a local earthquake using S-P times while the second exercise shows how to get data from international data bases.

Exercise 1

Manual location using S-P times

Use the arrival times read for the local event in exercise 1.

-Assuming a P-wave velocity of 7.0 km/sec and Vp/Vs = 1.73, determine the distance to each station using only first arrivals and the S-P arrival  times.

-Locate the earthquake by drawing circles,  the station map is found in Figure 2.1. Give the latitude and longitude of the epicenter.

-Evaluate the error in the epicenter location.

-Will the clock problem found for one of the station in exercise 1.2 affect the solution ?

Exercise 2

Manual location using origin time

The origin time was determined in exercise 2.1.

-Using a P-velocity of 7.0 km/sec, calculate the epicentral distances, how do they compare to the distances calculated in exercise 1 ?

-Locate the earthquake as above, how does the location compare the location in the previous exercise ?

-Will the clock problem found for one of the station in exercise 1.2 affect the solution ?

Exercise 3

Get data from international data bases

The most comprehensive location for information about epicenters anywhere in the world is the International Seismological Center (ISC). Connect to ISC www.isc.ac.uk.

-Select events in are 59-62 N and 0-10 E for the time period January to June, 1999

-Make a map of the epicenters using the ISC program on the web site.

-Extract the readings for the first event in the list

-Repeat above for events in an area of your own interest

Connect to the USGS earthquake information system http://neic.usgs.gov/.

-Find list of most recent earthquakes, print map

-Find largest earthquake in the last 5 days, give detailed information

Figure 2.1 Station map. Location of some of the stations in Western Norway. The map has the same scale in y and x the scale can be determined knowing that one deg latitude is 111 km.

Figure 2.1 EXTRA COPY.  Station map. Location of some of the stations in Western Norway. The map has the same scale in y and x the scale can be determined knowing that one deg latitude is 111 km.

EXERCISE  3

# Introduction to SEISAN

This exercise has the purpose to get an introduction to how to use computers for data processing. In previous exercises, some of the basic parameters have been described: Seismic phases and earthquake location. Still to be described is the magnitude of seismic events, the fault plane solution and spectral parameters. These are the basic parameters. A seismic processing system must handle all these and more parameters for many events. In addition, the original seismograms are in digital form, not paper records as seen so far. The SEISAN system can store and process all of this. In this exercise the user will get an introduction to the basic data base operation and how to do simple data manipulation.

Background material: SEISAN manual and Appendix 3.

Exercise 1

The SEISAN exercises 1-4 is done. All questions must be answered and plots given in the report.

EXERCISE  4

Picking phases and doing earthquake location using the computer

Manual earthquake locations have already been done. In practice all phase picking and earthquake location is done with a computer. In this exercise, both a local and a global events will be processed doing phase picking and location. The local event is located using a flat layered crustal model while the distant event is located using the IASP91 travel time table.

Exercise 1

-Do all exercises in SEISAN exercise 5, answer all questions.

Exercise 2

-Do SEISAN exercise 12, ‘Wadati diagram’

EXERCISE  5

# SEISMOGRAMS AND RESPONSE FUNCTION

Raw seismograms do not record the ground motion in displacement, velocity or acceleration directly. The aim of the exercise is to calculate true ground motion from seismograms.

Seismic instruments can be divided into analog and digital instruments. In this exercise we will first deal with analog seismographs, then with digital instruments.

The seismograph can be understood as a linear system where the input is the ground motion (displacement) and the output is the displacement on the seismogram. This can be visualized as follows

Input of ground motion   --> seismograph  --> seismogram

Mathematically we can write:

Aout(f)  =  Ain(f) * Gain(f)

where Aout is the output amplitude, Ain the input amplitude and Gain the gain of the seismograph, all values are frequency dependent. A typical gain curve for a classical analog seismograph is seen in Figure 5.2. The analog seismograph will consist of several elements each contributing to the gain, however the combined gain curve is often what is given. In the exercise, we know Aout and can therefore calculate Ain as

Ain(f)  =  Aout(f)/Gain(f)

Digital seismographs can in principle be described in a similar way giving just one gain curve. Since digital systems has the possibility to digitally process the data, the gain curve or gain function will normally be complex to take into account the phase response. In this exercise we will calculate the gain function using the individual elements of the seismic system:

Ground motion -> seismometer -> amplifier -> filter -> A/D converter ->  Output number

Each unit will linearly treat the signal so the complete gain for ground velocity Gv can be written:

Gv(f) = Gseism (f) * Gamp(f) * Gfilt(f) * Gconv(f)

Gseism is the gain of the seismometer. At a given frequency the gain could have been expressed as V/m, however, almost all electrodynamic seismometers have a flat response for velocity for frequencies above the natural frequency so gain constants for seismometers are expressed in terms of gain as a function of ground velocity. The gain constant is called seismometer generator constant and has the unit of V/(m/s). In a seismic system, it would also be possible to use an accelerometer as a sensor, which has a flat response for acceleration. The gain constant for an accelerometer is expressed in terms of V/g where g is the gravitational constant.

Gamp is the gain of the amplifier. The gain has the unit V/V (Volt in and Volt out) or number of times it amplifies. It is often expressed in dB which is 20*log(gain).

Gfilt is the filter gain. In terms of amplitude it is here assumed to have unity gain, but the filter will change the phase response. The filters used here are assumed to be Butterworth filters. The filter frequency, whether it is high pass or low pass must be known as well as the steepness of the filter. The steeper the filter, the more it filters and the steepness is measured in number of poles. For a low pass filter with e.g. 2 poles, the amplitude will decay as 1/(f*f) when f is above the filter corner frequency. The unit is the same as for an amplifier.

Gconv is the gain of the A/D converter (analog to digital converter). This unit converts the analog signal to a number to be used in the following digital processing. This number is often called the count value or just counts.

Remember that the relationships between displacement, velocity and acceleration are:

velocity = 2 * π * displacement*f

acceleration = 2 * π * velocity*f

This implies that the relationship between the gain functions for velocity and displacement, Gd is

Gv = Gd/2πf

Exercise 1

Instrument correction for a LP and SP record

Figure 5.1 and 1.2 respectively gives a short period and long period records of an earthquake and the response curves are found in Figure 5.2.

-Read maximum, amplitude and corresponding period on the SP and LP seismograms.

-Using the response curve, calculate the corresponding ground displacement, velocity and acceleration. Remember to use the gain given on the seismograms to select the correct response curve (peaks at 1 and 25 secs for SP and LP respectively). Do interpolation if needed. It is convenient to calculate the amplitudes in nm or um (micrometers).

Exercise 2

Correction of a broad band record

Figure 5.3 shows seismograms from a broad band station and Table 5.1 the response function. Calculate peak ground displacement for the earthquake by reading the maximum amplitude on the seismograms. Use the component with the largest amplitude. Note that the maximum count for each trace is shown on the seismogram.

Exercise 3

Manual gain calculation

Given a seismic station with the following characteristics;

Seismometer free period:     	1.0 sec

Damping ratio                	0.7

Loaded generator constant:   	200 V/m/s

Amplifier gain           :    	10 000

Filter        :		            A low pass filter at 30 Hz, gain 1

Recording media gain     :    	1000 counts/V

- Calculate manually the system gain at 10 Hz in terms of counts/(m/s) and counts/m.

Exercise 4

Correcting digitally for response

In SEISAN it is possible to remove the effect of the instrument and generate a seismogram showing displacement in nm. This is done in picking mode in mulplt. The requirement is that the response file is present in the system.

- Where is the response file and how is it made ? Print an example of the text response file.

Chose the local earthquake (June 25 3:36, 1996) and generate the true ground motion signal (option Groun). Since the instrument is short period, you cannot correct for the response down to very low frequencies and a filter must be chosen at the same time as the instrument removal is done. Make displacement, velocity and acceleration signals without a filter.

-How do the signal look, all reasonable ? If not, why ?

Use a filter 0.1 to 10 Hz and make all 3 signals.

-How do the signal compare to the above without filter ?

-How do the frequency content compare in the 3 types of signals.

Present plots of the results in your report, do not forget to put on units..

Table 5.1  Response curve for station NRS. The unit for the amplification is counts/nm and degrees for the phase. The frequency is in Hz.

Figure 5.1 SP seismogram. The figure shows a SP seismogram from the WWSSN. The gain is 25 000. The time scale on printed paper is 60mm/min like the original seismogram.

Figure 5.2  WWSSN displacement response curve. The maximum gain on the curve corresponds to the gain given on the seismogram.

Figure 5.3  A broad band seismogram The time scale is 20 sec/mm or 2 min between tics. The start time is June 28, 1992 at 11:57 38.039.

# EXERCISE 6

MAGNITUDE AND b-VALUE

The purpose is to calculate magnitude both manually and by computer and use magnitude statistics to calculate earthquake recurrence (b-value).

Exercise 1

Coda magnitude

The simplest magnitude to use for local earthquakes is the coda magnitude (also called duration magnitude). The coda length (tcoda) is defined as the total duration in seconds of the earthquake recording. The end of the record is most easily seen on filtered records or if the record is zoomed near the end of the recording.

Coda waves are scattered waves radiating from the earthquake hypocenter. Figure 6.1 shows how scattered energy arrives.

Figure 6.1  Development of P-wave coda due to scattering. Left: The enrergy arrives directly to the station STA from the hypocenter EQ, this is the direct P-wave. Center: Scattered energy arrives after the first P-arrival. If the scattering takes place further away (right), scattered energy arrives even later, however with a smaller amplitude.

At some time, the amplitude of the scattered arrival is smaller than the amplitude of the background noise and this is considered the end of the coda. If the initial amplitude of the signal is larger (a larger magnitude), the coda length will also be larger so this explains why the coda length is proportional to the earthquake magnitude. The strongest amplitude of the earthquake signal is the S-waves, so usually it is the S-wave scattered energy that is observed at the end of the signal.

The decay of amplitude of the scattered signal is inversely proportional to the distance it has travelled, in other words, the theoretical amplitude of the scattered will be inversely proportional to the travel time tc of the coda wave (time from origin time t0 to arrival time t):

tc = t – t0                                          				(6.1)

and ideally we should use tc to measure the magnitude, which can be expected to only depend on tc. The coda magnitude scale could then be expected to have the form

Mc = a Log( tc) + c						(6.2)

where a and c are constants. However, the coda length tcoda is traditionally measured from the P-arrival time tp to the end of the signal

tcoda = t –tp							(6.3)

By inserting 6.1 in 6.3 we then get

tcoda = tc –(tp –t0)						(6.4)

The measured coda length tcoda is therefore too short compared to the true coda length tc and the further the station is away from the earthquake, the smaller becomes tcoda for the same event, since tp increases with distance. To correct for the use of tcoda instead of tc, a compensation must therefore be made for distance and we can expect the scale to look like

Mc = a log(tcoda) + b dist +c					(6.5)

where dist is the hypocentral distance and b is a constant.

- Given the seismograms in Figure 6.1, determine the coda wave magnitude Mc for each station using the relationship

Mc = 2.6 * log tcoda  +  0.001 * dist(km) - 3.0

The distances dist come from exercise 2.

-Calculate the average magnitude.

-How sensitive is the magnitudes to coda lengths ?

Exercise 2

Local magnitude Ml

The local magnitude Ml is defined as

Ml = log(A) + Q(dist)

Where A is the maximum amplitude on a Wood-Anderson seismogram (displacement record) in mm and Q(dist) is a distance correction function. The distance correction function for California is given in Table 6.1.

Figure 6.2 shows the displacement seismogram for the local event used in exercise 2. The units of displacement is in nm. The gain of the Wood Anderson seismograph is 2180.

-Read the peak displacement for the stations on Figure 6.2.

-Convert to amplitude on a Wood-Anderson seismogram

-Calculate Ml for all stations

-Compare to the Mc values and evaluate

Exercise 3

Manual determination of Mb and Ms

Ms is calculated from the maximum surface wave amplitude on the vertical trace using the formula

Ms = log(A/T) + 1.66log (delta) +3.3

where A is the maximum amplitude in micrometers, T is the period in seconds and delta is the epicentral distance in degrees. Magnitude mb is calculated as

Mb = log(A/T) + Q(delta,h)

where A is the maximum amplitude in the P-wave train (fist 60 seconds) in nm, delta is the epicentral distance in degrees and h the focal depth in km. Q is a calibration function found in Figure 6.4.

-Calculate Ms for the event in Figure 5.3 (use results from exercise 5). Assume a shallow depth. The distance can be calculated using the location given on the plot and Figure 7.2

-Calculate Mb for event in Figure 6.3  Assume a  depth of 33 km and calculate distance from Figure 7.2.

-Compare to the reported values (can be found in ISC printed bulletin or on ISC web site), try to explain any deviations.

Exercise 4

b-value

Table 6.2 gives a catalog of earthquakes for Western Norway.

-Calculate number of earthquakes in 0.2 magnitude intervals (use coda magnitude), and the accumulative numbers N. Show table.

-Plot logN vs M and determine the b-value using coda magnitude. Give the relation with both a and b.

-How often will you statistically get a M ≥ 6 earthquake ?.

-Can the detection threshold be estimated ?.

Do SEISAN exercise 6

Table 6.1   The distance correction table for Southern California. Dist is the epicentral distance in km and Q(dist) the distance correction.

Year Date HRMM  Sec Latitud Longitud Depth   Mc   Ml

2003  7 2 1237 56.6  59.246    6.105   9.4  0.9

2003  710 1303  7.0  59.292    5.616  11.5  1.4  1.2

2003  718 1930 22.1  60.871    5.005   0.0  1.4  1.1

2003  721 1428 57.4  60.952    1.437  15.0  2.5  1.5

2003  722 0335 26.3  60.927    1.627  15.0  2.2  1.4

2003  729 1542 37.7  60.696    3.744  15.0  2.3  2.5

2003  8 2 1912 41.6  60.108    7.204  19.7  1.1  1.0

2003  8 4 1943 52.6  60.692    5.507   0.1  1.0  0.6

2003  811 1349 42.5  60.291    4.894  52.3  0.8  1.5

2003  812 1537 15.1  60.192    2.486  15.0  1.8  1.3

2003  821 0723  1.4  60.086    4.791   0.0  2.2  2.0

2003  821 1159  3.0  60.839    5.029   0.6  1.4

2003  825 1321 21.6  59.904    6.958   3.9  0.8

2003  825 1823 18.0  59.281    5.298  20.0  1.3  1.1

2003  827 1621 32.5  59.075    5.812   0.0  1.8  1.8

2003  828 1501 42.5  60.694    5.594   0.0  1.3

2003  9 3 1334 38.5  59.242    5.706  13.1  1.6

2003  9 4 1402 21.2  60.863    4.987  15.0  1.2  0.8

2003  9 5 1440  2.0  60.567    4.966   0.0  0.6  0.7

2003  9 5 2117 57.1  59.474    5.675  15.0  2.2  1.9

2003  9 8 1027 15.2  59.646    5.581   0.0  1.5  1.0

2003  9 9 1332 36.6  59.211    6.178  15.6  1.3  1.0

2003  9 9 1803 53.0  60.691    5.378   0.1  1.6  0.8

2003  912 1619 11.9  60.443    4.815   0.6  1.3  1.4

2003  917 0155 30.4  59.604    7.316  15.3  1.7  1.4

2003  917 1435 41.7  59.349    6.077   0.3  1.5  1.1

2003  918 1806 38.7  59.759    7.061  17.5  1.3

2003  919 0818  2.0  60.040    4.719   0.0  2.0  2.1

2003  920 1315 42.4  60.247    5.216  12.4  1.0  1.4

2003  920 1709 20.5  59.694    7.087  15.5  1.4

2003  925 1131 45.7  60.466    5.407   0.0  0.8

2003  928 1654 54.1  60.000    5.861   0.0  1.4  1.2

2003  928 2025  8.4  60.346    4.738   0.0  1.7  1.5

2003  929 1552 29.2  60.290    5.128   0.0  1.0

2003 10 2 1330 35.3  59.153    6.200  15.0  1.3

2003 10 2 1611  4.4  60.817    4.912   0.1  1.5  1.0

2003 10 9 0108  0.9  60.163    5.314   0.1  1.2  1.3

2003 1014 1355 39.1  60.501    4.919   0.0  1.5  0.9

2003 1020 0508 10.6  60.417    6.012  13.0  0.9  0.9

2003 1020 1331 16.0  59.378    6.034  13.8  1.4

2003 1020 1620 21.0  59.150    7.611  11.3  1.7

2003 1021 1432 41.3  60.674    5.460   0.0  1.6  0.9

2003 1022 1400 44.5  60.519    4.944   0.0  1.3

2003 1023 1419 18.9  60.300    5.295   3.5  1.1

2003 1028 1803 55.8  60.758    5.242   1.5  1.2

2003 1031 1605 51.0  60.832    5.013   9.2  1.5

2003 11 6 0343 50.8  60.747    4.573   0.0  0.9  1.1

2003 11 9 0459 58.9  59.619    7.105  12.6  1.6  0.8

2003 1110 2302 54.9  59.215    5.805   0.0  1.2  1.0

2003 1113 1301  3.6  60.512    5.349   0.0  0.7  1.4

2003 1113 1306 21.2  60.677    5.487   0.1  1.4  0.8

2003 1120 1109 31.8  59.333    5.657   2.3  1.6  1.2

2003 1121 1310  8.1  60.477    5.350   0.0  0.5  0.8

2003 1122 1908 58.2  60.218    2.545  15.0  2.6  2.2

2003 1125 1832 15.8  59.665    2.465   0.0  1.9  1.1

2003 1127 0317 49.6  59.914    6.215   0.0  0.7  0.6

2003 1128 1252  0.6  60.276    5.301   6.2  0.2  0.5

2003 1128 1529 31.3  60.189    5.312  11.4  0.8  0.8

2003 12 1 1404  6.6  60.713    5.339   0.0  1.6  1.1

2003 12 1 1501 52.0  60.162    5.237  16.1  0.7  0.4

2003 12 4 1449 16.1  60.544    4.959   0.1  1.4  1.3

2003 12 8 2353  9.8  60.323    7.252   3.1  1.8  1.7

2003 12 9 1400  1.2  59.492    4.473   0.1  1.2  1.6

2003 1211 1404 50.0  60.291    5.294   0.0  0.8  1.1

2003 1211 1454 29.8  60.695    5.568   1.8  1.4  0.8

2003 1212 0007 13.4  60.489    4.734  21.1  1.1  1.0

2003 1212 0315  6.7  59.857    6.523   0.0  1.5  1.3

2003 1212 1516  7.0  60.846    5.102   1.5  1.4  0.6

2003 1217 1433 40.9  59.315    5.675   0.0  1.5  1.1

2003 1219 1020 30.0  59.376    6.078   0.1  1.1

2003 1219 1328 25.4  60.669    5.558   0.1  1.5

2003 1225 1400 27.7  59.655    6.000  15.0  1.9  1.8

Table 6.2  Catalog of events

Figure 6.1  Seismogram of a local earthquake, same as in exercise 2

Figure 6.2  Wood Anderson simulated displacement seismogram. The number above traces to the right is maximum amplitude in nm.

Figure 6.3  P-wave for a distant earthquake recorded in S. Norway. The vertical scale is nm and the maximum amplitude is marked above the trace to the right. The origin is 1996 0603 1955 31.8, the hypocenter has latitude 46.787 N, longitude 153.722 W  and depth 33.0 km. The time scale is 2 mm/sec.

Figure 6.4   Calibration function for mb. It is assumed that the amplitude is measured in nm.

EXERCISE 7

Using a single station or array for azimuth determination

The purpose of this exercise is to locate an event with a single three component station or an array.

Global phases are best recorded on standard LP and SP seismographs sine most of the energy is below 1 Hz. On high gain local networks, a few global events are also located. Global (and local) events can be located with a single 3C station or a seismic array. The 3C location method is described in Appendix 2.

Using a seismic array, the apparent velocity and azimuth to the event can be determined as follows: Considering a plane wave arriving at the 3 stations shown below at times t0, t1 and t2, then the following equations can be set up:

Figure  7.1  A 3 station array. The station are labeled  0,1,2 and station 0 is placed at the origin of the coordinate system. The vectors from the origin to station 1 and two are labeled  r1 and r2 respectively and Az is the azimuth of arrival.

t1 - t0 = r1 * p			 			                                   (1)

t2 - t0 = r2 * p

where r1 and r2 are the vectors form station 0 to station 1 and 2 respectively and p is the slowness vector defined as p=s/v, where s is the normal vector to the wave front and v the apparent velocity. Equation 1 can be written out as

t1 - t0 = r1x * px  +  r1y * py                 					(2)

t2 - t0 = r2x * px  +  r2y * py

where px and py are the x and y components of the p-vector and corresponding for r1x etc. Thus knowing the arrival times at the 3 stations, px and py can be determined (2 equations with 2 unknowns). From px and py, v and azimuth can be determined:

tan(Az) = px/py

v = sqrt (1/(px*px + py*py))

Note that the azimuth above is away from the event, while the azimuth needed to find the epicenter is from the station to the event and 180 deg must be added. Since it is possible to get the epicentral distance from the apparent velocity, a location can be made.

Exercise 1

Azimuth and velocity from a three station array

An array has the following station location (coordinates in km):

Station 0  (0,0)

Station 1  (100,10)

Station 2  (10,200)

A P-wave is arriving at times t0=0 sec, t1= 7 sec and t2= 13 sec.

-Calculate the azimuth and apparent velocity.

-From the Bullen table, get the distance to the earthquake. Remember that the Bullen table gives the apparent velocity in sec/degree, so the easiest is to convert from km/sec to sec/deg before looking up in the table (1 degree = 111.1 km). Note that the first part of the table has entries for every 0.5 degrees. Assume a depth of 33 km.

-Use Figure 7.2  to get an approximate location assuming the array is located in Bergen.

-Describe how you would find px and py if you had e.g. 10 stations.

Exercise 2

Azimuth from a three component station

-Using the 3C seismogram in Figure 7.3, calculate the az of approach. Note that the scale of the 3 traces are different.

-Read the S-P time on Figure 7.4 and find the distance from Bullen or a travel time curve assuming a depth of 33 km..

-Locate the event using Figure 7.2 and give latitude, longitude and origin time.

-Compare to the real solution (found e.g. in ISC bulletin) and plot it on the figure.

Exercise 3

Azimuth determination by computer

-Do SEISAN exercise 12, ‘3 component analysis for azimuth determination’. Describe results and uncertainties in determination.

Figure 7.2  World map

Figure 7.2  World map, extra copy

Figure 7.3  A three component recording, only the first P is shown. The time scale is 20 mm/sec. The numbers above the traces to the right are the maximum amplitudes in counts and the numbers to the left the DC level. When reading the amplitudes on the paper, they have to be corrected different maximum amplitude on the 3 traces.

Figure 7.4  The complete cording of the event in Figure 7.2. A filter is used to enhance the low frequencies. The time scale is 20 mm/min.

EXERCISE 8

FAULT PLANE SOLUTION

In this exercise, fault plane solutions will be determined both manually and with SEISAN for both local and global events. Background material is found in Appendix 2 including a stereo net.

Exercise 1

Manual fault plane solution for a local event

Do exercise 3.2 in Appendix 2, task 1-7, 9, 12-14.

Exercise 2

Manual fault plane solution from a distant event

Table 8.1 is an earthquake bulletin for ISC. Only stations which reported polarity (p or d) are given.

Get angle of incidence from distances using Table 8.2. For stations at distances less than 20 deg., calculate the angle assuming all phases to be Pn and the Moho velocity is 8 km/s and the velocity above Moho is 7 km/s. Then plot on a stereo net and find the fault plane solution. Put the T and P-axis on the solution. Measure the angles of the 2 fault plane solutions and the T and P-axis. From the angles of the P and T axis, calculate strike, dip and rake using the Focmec program type focmec a. Compare to the solution given by ISC by plotting the solution on the same figure.

-Which kind of fault do the solution represent.

Exercise 3

Fault plane solution done by computer

Do SEISAN exercise 7

rms   OT_error      Smajor Sminor Az        Err   mdist  Mdist     Err        Err        Err     Quality

2000/01/06 10:42:22.8     58.0180 -141.0300      1.0 f          5 351  MS 5.7     mb 5.1     mb 5.5     BER        3544558

1.60   +-  4.86      94.3  581.3   -1

2000/01/06 10:42:25.0     58.0000 -136.9000      5.0           58      Ms 6.5        6.1     mB 5.9     BJI        3017104

1.70

2000/01/06 10:42:25.0 f   58.0400 -136.8700 f    1.0 f        371  31     5.9 73  Me 6.2     Mw 6.1     NEIC       3050653

1.29 150.19                                       fe

(#FAULT_PLANE Typ Strike   Dip    Rake  NP  NS Plane Author   )

(#            BB  345.00 78.00 -178.00               NEIC     )

(+            BB  255.00 88.00  -12.00               NEIC     )

(#PRINAX sc  T_val T_azim  T_pl  B_val B_azim  B_pl  P_val P_azim  P_pl Author   )

(#                 300.00  7.00          0.00  0.00        209.00 10.00 NEIC     )

(#MOMTENS sc    MO fCLVD    MRR    MTT    MPP    MRT    MTP    MPR NST1 NST2 Author   )

(#             eMO eCLVD    eRR    eTT    ePP    eRT    eTP    ePR NCO1 NCO2 duration )

(#        18 1.500        0.170 -0.950  0.780  0.120  1.180 -0.080   43      NEIC     )

(#                                                                                    )

(#FAULT_PLANE Typ Strike   Dip    Rake  NP  NS Plane Author   )

(#            BDC 252.00 86.00   -3.00               NEIC     )

(+            BDC 342.00 87.00 -176.00               NEIC     )

(#PRINAX sc  T_val T_azim  T_pl  B_val B_azim  B_pl  P_val P_azim  P_pl Author   )

(#       18  1.380 117.00  1.00  0.180  16.00 85.00 -1.560 207.00  5.00 NEIC     )

(Depth from synthetics of broadband displacement seismograms. Energy computed from BB mechanism.)

(After preliminary solution from PGC.)

(Felt strongly at Elfin Cove, Gustavus, Haines, Hoonah, Juneau and Sitka. Also felt at Petersburg, Skagway and Yakutat. Felt as far a)

( Whitehorse, Yukon Territory)

(#PARAM BROADBAND_DEPTH=12.0 SEISMIC_ENERGY=4.8E13+0.7E13)

2000/01/06 10:42:25.8     58.0680 -136.8081      1.0 f     9    6      ML 6.1  4                        PGC        3443410

0.37                  3.3    1.8   -1                             +-0.2                               ke

(Coast of southeastern Alaska.)

2000/01/06 10:42:27.0     58.2071 -136.7483      0.0 f    21   17 155  ML 4.8  3  MS 5.8 11  mb 4.9 11  EIDC       3009581

0.73   +-  0.77      19.1   12.0   33               3.55 147.87   +-0.4      +-0.1      +-0.1         uk

2000/01/06 10:42:29.4     58.2074 -136.7458     33.0      28   28      Mb 5.5 31  Ms 5.9  6             LDG        3029562

+-  0.42      21.4   14.7   11    +-  0.0   61.97  98.38   +-0.2      +-0.1                    ke

2000/01/06 10:42:29.8     58.1230 -136.9790     33.0     109           MS 5.8 34  mb 5.7 31             MOS        3023607

+-  1.07      11.5    4.1   21

2000/01/06 10:42:32.8     58.2700 -136.8000                            Mw 6.1                           HRVD       3050654

+-  0.10       0.0    0.0   -1                                                                 se

(#CENTROID)

(#MOMTENS sc    MO fCLVD    MRR    MTT    MPP    MRT    MTP    MPR NST1 NST2 Author   )

(#             eMO eCLVD    eRR    eTT    ePP    eRT    eTP    ePR NCO1 NCO2 duration )

(#        18 1.600       -0.120 -0.840  0.960  0.800  1.030 -0.160   60   55 HRVD     )

(#                        0.010  0.010  0.010  0.040  0.010  0.040  151  105     5.40 )

(#FAULT_PLANE Typ Strike   Dip    Rake  NP  NS Plane Author   )

(#            BDC 343.00 65.00 -166.00               HRVD     )

(+            BDC 247.00 77.00  -25.00               HRVD     )

(#PRINAX sc  T_val T_azim  T_pl  B_val B_azim  B_pl  P_val P_azim  P_pl Author   )

(#       18  1.460 297.00  8.00  0.260  42.00 62.00 -1.720 203.00 27.00 HRVD     )

(Data Used: GSN.)

(#PARAM pP_DEPTH=15)

2000/01/06 10:42:44.5     60.7430 -140.4150      1.0 f          5      mb 4.6                           NAO        3544559

2000/01/06 10:42:55.1     61.8000 -134.1000     10.0      27   27 358  mb 5.9 27                        ZUR        3529774

0.26                                               66.75  68.36   +-0.3                               uk

2000/01/06 10:42:25.3     58.1340 -136.9340      1.0 f   476  515 117  MS 5.9     mb 5.5                ISC        3630399

1.14   +-  0.13       2.6    2.3   90               1.38 157.06                                   m i

(#PARAM pP_DEPTH=8.7+1.64 )

SOUTHEASTERN ALASKA

ta     Dist  EvAz     Phase      Date       Time     TRes  Azim  AzRes  Slow

HYT     2.71 354.1  d  PN      2000/01/06 10:43:11.1   0.3

WHY     2.74  21.6  d  PN      2000/01/06 10:43:11.5   0.3

BNAB    5.85 140.0  c  PN      2000/01/06 10:43:51.6  -3.6

DAWY    6.07 349.7  d  PN      2000/01/06 10:43:58.0  -0.4

BMBC    8.33  98.2  d  P       2000/01/06 10:44:27.2  -2.9

DOWB   12.49 114.1  c  P       2000/01/06 10:45:25.7  -1.2

PNT    13.49 123.4  c  P       2000/01/06 10:45:40.6   0.3

ULM    24.94  90.5  d  P       2000/01/06 10:47:50.4  -0.6

KLR    50.79 302.2  di P       2000/01/06 10:51:28.7   0.0

BOD    51.35 319.6  ci P       2000/01/06 10:51:32.6  -0.2

IRK    59.21 321.2  ce P       2000/01/06 10:52:29.0  -0.8

SNY    60.14 301.8  d  P       2000/01/06 10:52:34.2  -2.2

MOY    60.80 322.8  ce P       2000/01/06 10:52:41.3   0.6

UKR    66.06 332.6  ci P       2000/01/06 10:53:14.5  -0.7

MOS    66.40   3.4  ci P       2000/01/06 10:53:13.9  -3.4

CLL    68.18  19.8  c  P       2000/01/06 10:53:28.8   0.1

SLE    70.67  23.9  de P       2000/01/06 10:53:43.5  -0.5                6.4

BOURR  70.75  24.9  de P       2000/01/06 10:53:44.7   0.2                6.4

ZLA    70.92  24.1  de P       2000/01/06 10:53:45.4  -0.1                6.4

KAMOR  71.33  23.4  de P       2000/01/06 10:53:48.6   0.6                6.4

APL    71.39  24.4  de P       2000/01/06 10:53:48.7   0.3                6.4

BNALP  71.50  24.3  de P       2000/01/06 10:53:49.9   0.8                6.4

HASLI  71.55  24.5  de P       2000/01/06 10:53:50.0   0.6                6.4

LLS    71.65  23.9  de P       2000/01/06 10:53:50.3   0.4                6.4

LLS    71.65  23.9  de P       2000/01/06 10:53:50.6                      6.4

AIGLE  71.68  25.5  de P       2000/01/06 10:53:50.2   0.1                6.4

DAVON  71.83  23.4  de P       2000/01/06 10:53:52.1   1.1                6.4

FUSIO  71.95  24.3  de P       2000/01/06 10:53:52.7   1.0                6.4

BOG    72.00 111.1  ci P       2000/01/06 10:53:57.5   4.9

DIX    72.03  25.2  de P       2000/01/06 10:53:52.8   0.6                6.4

DIX    72.03  25.2  de P       2000/01/06 10:53:53.2                      6.4

OSS    72.05  23.2  de P       2000/01/06 10:53:52.9   0.6                6.4

VDL    72.09  23.7  de P       2000/01/06 10:53:53.8   1.2                6.4

MMK    72.18  24.9  de P       2000/01/06 10:53:54.4   1.3                6.4

MCGN   72.27  24.9  c  P       2000/01/06 10:53:55.3   1.6

BERNI  72.28  23.3  de P       2000/01/06 10:53:54.9   1.2                6.4

WHN    73.63 301.6  d  P       2000/01/06 10:54:01.6  -0.2

ASS    76.02  22.5  c  P       2000/01/06 10:54:15.9   0.6

MNS    76.69  22.6  c  P       2000/01/06 10:54:19.3   0.2

NURP   85.83 332.6  ci P       2000/01/06 10:55:04.2  -3.1

SHL    87.23 317.1  ci P       2000/01/06 10:55:14.0  -0.3

Table 8.2   ISC bulletin, extract.

# EXERCISE 9

SPECTRAL ANALYSIS

The purpose is to determine common spectral parameter: Seismic moment, corner frequency, source size and stress drop.

Exercise 1

Manual spectral analysis

Do exercise 3.4 from Appendix 2

Exercise 2

Spectral analysis of a local event using SEISAN

-Do SEISAN exercise 8, give screen dumps of results.

Exercise 3

Velocity and acceleration spectra

-Using the event for exercise 2, select a good station and make the velocity and acceleration spectra. Do not use station KONO since it has a low sample rate. Limit the frequency band of spectrum to range with good signal to noise ratio.

-Explain how spectra are expected to look and why.

-Do the spectra look as expected ?

-What is the y-axis unit of all 3 types of spectra ?

Question 4

Spectrum and Q

The spectral shape is dependent on the Q-values used for spectral correction. Make the S-wave displacement spectrum for the signal used for one station under exercise 2 using Q0=10 and Q0=100 and qalpha=0.5. The Q-value is changed in file MULPLT.DEF in directory DAT.

-Compare the spectral values and spectral shape and explain any differences.

# EXERCISE 10

Analysis of a set of local events

Using the skills acquired in previous exercises, a set of 10 local events will be used to do a comprehensive analysis. The data set consists of 10 waveform files, a station file and calibration files.

Exercise 1

Create a data base with a name of your choice, register the events into the data base. Install calibration files and station files.

Exercise 2

Locate all events and calculate Mc, Ml and Mw, check all events for reasonable fit, RMS should be less than 1.0 s. Check that, for each event, that there is a consistency between different types of magnitudes.

Exercise 3

Make an epicentral map.

Exercise 4

Compare the magnitude types obtained using program mag. This mens plotting Ml versus Mc and Ml versus Mw. How is the comparison ?

## References

Bormann, P. (2002) IASPEI New Mnaual of Seismological Observatory Practice, GFZ Potsdam.

Kulhanek, O. Anatomy of seismograms, Elsevier

Payo, G. (1986) Introducion al analysis de sismogramas, Published by  Instituto Geografico Nacional, Spain.

| Topic | Earthquake location |
| --- | --- |
| compiled by | Jens Havskov, University of Bergen, Institute of Solid Earth Physics, Allégaten 41, N-5007 Bergen, Fax: +47 55 589669, E-mail: jens@ifjf.uib.no Peter Bormann, GeoForschungszentrum Potsdam, Telegrafenberg, D-14473 Potsdam, Germany; Fax: +49 331 288 1204; E-mail: course@gfz-potsdam.de Johannes Schweitzer, NORSAR, P.O.Box 53, N-2027 Kjeller, Fax: +47 63818719, E-mail: johannes.schweitzer@norsar.no |
| Version | May, 2002 |

## 1	Introduction

The exact location of a source, radiating seismic energy, is one of most important tasks in practical seismology and most seismologists have been from time to time involved in this task. The intention with this document is to describe the most common location methods without going into the mathematical details, which have been described in numerous textbooks and scientific, but to give some practical advice on earthquake location.

The earthquake location is defined by the earthquake hypocenter (x0, y0, z0) and the origin time t0. The hypocenter is the physical location, usually given in longitude (x0), latitude (y0), and depth below the surface (z0 [km]). For simplicity, the hypocenter will be labeled x0, y0, z0 with the understanding that it can be either measured in geographical or Cartesian coordinates, i.e., in [deg] or [km], respectively. The origin time is the start time of the earthquake rupture. The epicenter is the projection of the earthquake location on the Earth’s surface (x0, y0). When the earthquake is large, the physical dimension can be several hundred kilometers and the hypocenter can in principle be located anywhere on the rupture surface. Since the hypocenter and origin time are determined by arrival times of seismic phases initiated by the first rupture, the computed location will correspond to the point where the rupture initiated and the origin time to the time of the initial rupture. This is also true using any P- or S-phases since the rupture velocity is smaller than the S-wave velocity so that P- or S-wave energy emitted from the end of a long rupture will always arrive later than energy radiated from the beginning of the rupture. Standard earthquake catalogs (such as from the International Seismological Center, ISC) report location based primarily on arrival times of high frequency P-waves. This location can be quite different from the centroid time and location obtained by moment tensor inversion of long period waves. The centroid location represents the average time and location for the entire energy radiation of the event.

### 2	Single station location

In general, epicenters are determined using many arrival times from different seismic stations and phases. However, it is also possible to locate an earthquake using a single 3-component station. Since the P-waves are vertically and radially polarized, the vector of P-wave motion can be used to calculate the backazimuth to the epicenter (see Figure 1). The radial component of P will be recorded on the 2 horizontal seismometers N(orth) and S(outh) and the ratio of the amplitudes AE/AN on the horizontal components can be used to calculate the backazimuth of arrival AZI:

AZI = arctan AE/AN						       (1)

There is then an ambiguity of 180( since the first polarity can be up or down so the polarity must also be used in order to get the correct backazimuth. If the first motion on vertical component of the P is upward, (which corresponds by definition to a compressional first motion (FM) arriving at the station related to an outward directed motion at the source then the radial component of P is directed away from the hypocenter. The opposite is true if the P-polarity is negative (see also Figure 1 in Exercise EX 11.2).

Figure 1  Example of P-wave first motions in 3-component records (left) from which the backazimuth AZI and incidence angle i can be derived according to Eqs. (1) and (2) (middle).

The amplitude AZ of the Z-component can, together with the amplitude AR = ( (AE2 + AN2) on the radial components, also be used to calculate the apparent angle of incidence iapp = arc tan AR / AZ of a P-wave. However, according already to Wiechert (1907) the true incidence angle itrue of a P-wave is

itrue = arcsin ( ( sin 0.5iapp),				    (2)

with the difference accounting for the amplitude distortion due to the reflection at the free surface. Knowing the incidence angle i and the local seismic velocity vc below the observing station, we can calculate the apparent velocity vapp of this seismic phase with

(3)

With high frequency data it might be difficult to manually read the amplitudes of the first break or sometimes the first P-swings are emergent. Since the amplitude ratio between the components should remain constant not only for the first swing of the P-phase but also for the following oscillations of the same phase, we can, with digital data, use the predicted coherence method (Roberts et al., 1989) to automatically calculate backazimuth as well as the angle of incidence. Since this is much more reliable and faster than using the manually readings of the first amplitudes, calculation of backazimuth from 3-component records of single stations has again become a routine practice (e.g., Saari, 1991). In case of seismic arrays, apparent velocity and backazimuth can be directly measured by observing the propagation of the seismic wavefront with array methods (see Chapter 9). As we shall see later, backazimuth observations are useful in restricting epicenter locations and in associating observations to a seismic event. Knowing the incidence angle and implicitly the ray parameter of an onset helps to identify the seismic phase and to calculate the epicentral distance.

With a single station we have now the direction to the seismic source. The distance can be obtained from the difference in arrival time of two phases, usually P and S. If we assume a constant velocity, and origin time t0, the P- and S-arrival times can then be written as

tp = t0 + D/vp                                  ts = t0 + D/vs				    (4)

where tp and ts are the P- and S-arrival times respectively, vp and vs are the P- and S-velocities respectively and D is the epicentral distance (near) for surface sources and the hypocentral distance for deeper sources. By eliminating t0 from Eq. (4), the distance can be calculated as

(5)

with D in km and ts – tp in seconds. But Eq. (5) is applicable only for the travel-time difference between Sg and Pg, i.e., the direct crustal phases of S and P, respectively. They are first onsets of the P- and S-wave groups of local events only for distances up to about 100 – 250 km, depending on crustal thickness and source depth within the crust. Beyond these distances the Pn and Sn, either head waves critically refracted at the Mohorovičić discontinuity or waves diving as body waves in the uppermost part of the upper mantle become the first onsets (see Fig. 7). The “cross-over” distance xco between Pn and Pg (or Pb) can be approximately calculated for a (near) surface focus from the relationship

xco = 2 zm ((vm –(vp) (vm +( vp)(-1/2,					(6)

with (vp – average crustal P-velocity, vm – sub-Moho P-velocity, and zm – crustal thickness. Inserting the rough average values of(vc = 6 km/s and vm =  8 km/s we get, as a “rule of thumb”, xco ( 5 zm. At smaller distances we can be rather sure that the observed first arrival is Pg. Note, however, that this “rule of thumb” is valid for surface focus only. As demonstrated with Fig. 2.40 in Chapter 2, the crossover distance is only about half as large for near Moho earthquakes and also the dip of the Moho and the direction of observation (up- or downdip) does play a role. However, in continental (intraplate) environment, lower crustal earthquakes are rare. Mostly they occur in the upper crust.

Examples for calculating the epicentral distance D and the origin time OT of near seismic events by means of a set of local travel-time curves for Pn, Pg, Sn, Sg and Lg are given in exercise EX 11.1. In the absence of local travel-time curves for the area under consideration one can use Eq. (5) for deriving a “rule of thumb” for approximate distance determinations from travel-time differences Sg-Pg. For an ideal Poisson solid vs = vp/. This is a good approximation for the average conditions in the Earth crust: With this follows from Eq. (5) : D = (tSg – tPg) ( 8.0 for “normal, medium age” crustal conditions with (vp = 5.9 km/s, and D = (tSg – tPg) ( 9.0 for old Precambrian continental shields with rather large (vp = 6.6 km/s. However, if known, the locally correct vp/vs ratio should be used to improve this “rule of thumb”. If the distance is calculated from the travel-time difference between Sn and Pn another good rule of thumb is D = (tSn – tPn) ( 10. It may be applicable up to about 1000 km distance.

For distances between about 20o < ( < 100o the relationship (o = ((ts – tp )min - 2( ( 10 still yields reasonably good results with errors < 3°, however, beyond D = 10° the use of readily available global travel-time tables such as IASP91 (Kennett and Engdahl, 1991; Kennett, 1991), SP6 (Morelli and Dziewonski, 1993), or AK135 (Kennett et al., 1995) is strongly recommended  for calculating  the distance.

With both backazimuth and distance, the epicenter can be obtained by measuring off the distance along the backazimuth of approach. Finally, knowing the distance, we can calculate the P-travel time and thereby get the origin time using the P-arrival time (see Exercise EX 11.2: Manual localization of teleseismic events by means of 3-component records).

#### 3	Multiple station location

  - Manual location

When at least 3 stations are available, a simple manual location can be made from drawing circles (the circle method) with the center at the station locations and the radii equal to the epicentral distances calculated from the S-P times (Figure 2).

These circles will rarely cross in one point which indicates errors in the observations and/or that we have wrongly assumed a surface focus. In fact, ts – tp is the travel-time difference for the hypocentral distance d which is for earthquakes with z > 0 km generally larger than the epicentral distance ( (or D). Therefore, the circles drawn around the stations with radius d will normally not be crossing in a single point at the epicenter but rather “overshoot”. One should therefore fix the epicenter either in the “center of gravity” of the overshoot area (black area in Figure 2) or draw “chords”, i.e., straight lines passing through the crossing point between two neighboring circles. These chord lines intersect in the epicenter (see Figure 1 in Exercise EX 11.1). Still other methods exist (e.g., Båth, 1979) to deal with this depth problem (e.g., the hyperbola method which uses P-wave first arrivals only and assumes a constant P-wave velocity), however since they are rarely used, they will not be discussed here.

Figure 2  Location by the “circle and chord” method. The stations are located in S1, S2 and S3. The epicenter is found within the shaded area where the circles overlap. The best estimate is the crossing of the chords, which connect the crossing points of the different pairs of circles.

With several stations available from a local earthquake, the origin time can be determined by a very simple technique called a Wadati diagram (Wadati, 1933). Using Eq. (7) and eliminating (, the S-P travel-time difference can be calculated as

ts – tp = (vp/vs – 1) ( (tp - t0)   						    (7)

The S-P times are plotted against the absolute P-time. Since ts – tp goes to zero at the hypocenter, a straight line fit on the Wadati diagram (Figure 3) gives the origin time at the intercept with the P-arrival axis and from the slope of the curve, we get vp/vs. Note that it is thus possible to get a determination of both the origin time and a mean vp/vs ratio without any prior knowledge of the crustal structure, the only assumption is that vp/vs is constant and that the P- and S-phases are of the same type like Pg and Sg or Pn and Sn. Such an independent determination of these parameters can be very useful when using other methods of earthquake location.

The Wadati diagram can also be very useful in making independent checks of the observed arrival times. Any points not fitting the linear relationship might be badly identified, either by not being of the same phase type or by misreading.

Figure 3  An example of a Wadati diagram. The intercept on the x-axis gives the origin time. The slope of the line is 0.72 so the vp/vs ratio is 1.72. Note that the points do not exactly fit the line, indicating model and/or data reading errors (from Lay and Wallace, 1995).

  - Computer location

Manual location methods provide insight into the location problems, however in practice we use computer methods. In the following, the most common ways of calculating hypocenter and origin time by computer will be discussed.

The calculated arrival time tic at station i can be written as

tic = T(xi, yi,, zi, x0, y0, z0) + t0					(8)

where T is the travel time as a function of the location of the station (xi, yi, zi) and the hypocenter. This equation has 4 unknowns, so in principle 4 arrival time observations from at least 3 stations are needed in order to determine the hypocenter and origin time. If we have n observations, there will be n equations of the above type and the system is over determined and has to be solved in such a way that the misfit or residual ri at each station is minimized. ri is defined as the difference between the observed and calculated travel times

ri = tio- tci .							(9)

In principle, the problem seems quite simple. However, since the travel-time function T is a nonlinear function of the model parameters, it is not possible to solve Eq. (8) with any analytical methods. So even though T can be quite simple calculated, particularly when using a 1D Earth model or pre-calculated travel-time tables, the non-linearity of T greatly complicates the task of inverting for the best hypocentral parameters. The non-linearity is evident even in a simple 2D epicenter determination where the travel time ti from the point (x, y) to a station (xi, yi) can be calculated as

,					(10)

where v is the velocity. It is obvious that ti does not scale linearly with either x and y so it is not possible to use any set of linear equations to solve the problem and standard linear methods cannot be used. This means that given a set of arrival times, there is no simple way of finding the best solution. In the following, some of the methods of solving this problem will be discussed.

3.2.1	Grid search

Since it is so simple to calculate the travel times of all seismic phases to any point in the model, given enough computer power, a very simple method is to perform a grid search over all possible locations and origin times and compute the arrival time at each station (e.g., Sambridge and Kennett, 1986). The hypocentral location and origin time would then be the point with the best agreement between the observed and calculated times. This means that some measure of best agreement is needed, particularly if many observations are used. The most common approach is least squares which is to find the minimum of the sum of the squared residuals e from the n observations:

(11)

The root mean squared residual RMS, is defined as . RMS is given in almost all location programs and commonly used a guide to location precision. If the residuals are of similar size, the RMS gives the approximate average residual. As will be seen later, RMS only gives an indication of the fit of the data, and a low RMS does not automatically mean an accurate hypocenter determination. Generally, the precision of the computational solution, which is based on various model assumptions, should not be mistaken as real accuracy of the location and origin time. This point will be discussed later under section 7.

The average squared residual e/n is called the variance of the data. Formally, n should here be the number of degrees of freedom ndf, which is the number of observations minus the number of parameters in fit (here 4). Since n usually is large, it can be considered equal to the number of degrees of freedom. This also means that RMS2 is approximately the same as the variance.

The least squares approach is the most common measure of misfit since it leads to simple forms of the equations in the minimization problems (see later). It also works quite well if the residuals are caused by uncorrelated Gaussian noise. However in real problems this is often not the case. A particularly nasty problem is the existence of outliers, i.e., individual large residuals. A residual of 4 will contribute 16 times more to the misfit e, than a residual of 1. Using the sum of the absolute residuals as a norm for the misfit can partly solve this problem:

.							(12)

This is called the L1 norm and is considered more robust when there are large outliers in the data. It is not much used in standard location programs since the absolute sign creates complications in the equations. This is of course not the case for grid search. Therefore, most location programs will have some scheme for weighting out or truncating large residuals (see later), which can partly solve the problem.

Once the misfits (e.g., RMS) have been calculated at all grid points, one could assign the point with the lowest RMS as the ‘solution’. For well-behaved data, this would obviously be the case, but with real data, there might be several points, even far apart, with similar RMS and the next step is therefore to estimate the probable uncertainties of the solution. The simplest way to get an indication of the uncertainty, is to contour the RMS as a function of x and y (2D case) in the vicinity of the point with the lowest RMS (Figure 4).

Figure 4 Left: RMS contours (in seconds) from a grid search location of an earthquake off western Norway (left). The grid size is 2 km. The circle in the middle indicates the point with the lowest RMS (1.4 s). Right: The location of the earthquake and the stations used. Note the elongated geometry of the station distribution. Its effect on the error distribution will be discussed under 4.1. The RMS ellipse from the figure on the left is shown as a small ellipse in the figure at right. Latitudes are degrees North and longitudes degrees East.

Clearly, if RMS is growing rapidly when moving away from the minimum, a better solution has been obtained than if RMS grows slowly. If RMS is contoured in the whole search area, other minima of similar size might be found indicating not only large errors but also a serious ambiguity in the solution. Also note in Fig. 4 that networks with irregular aperture have reduced distance control in the direction or their smallest aperture but good azimuth control in the direction of their largest aperture.

An important point in all grid-search routines is the method how the possible model space is searched through. In particular for events observed at teleseismic distances the model space can be very large. Sambridge and Kennett (2001) published a fast neighbourhood algorithm to use for global grid search.

3.2.2	Location by iterative methods

Despite increasing computer power, earthquake locations are mainly done by other methods than grid search. These methods are based on linearizing the problem. The first step is to make a guess of hypocenter and origin time (x0, y0, z0, t0). In its simplest form, e.g., in case of events near or within a station network, this can be done by using a location near the station with the first arrival time and using that arrival time as t0. Other methods also exist (see below). In order to linearize the problem, it is now assumed that the true hypocenter is close enough to the guessed value so that travel-time residuals at the trial hypocenter are a linear function of the correction we have to make in hypocentral distance.

The calculated arrival times at station i, tic from the trial location are, as given in Eq. (8), tic = T(x0, y0, z0, xi, yi, zi) + t0 and the travel-time residuals ri are ri = tio – tic . We now assume that these residuals are due to the error in the trial solution and the corrections needed to make them zero are (x, (y, (z, and (t. If the corrections are small, we can calculate the corresponding corrections in travel times by approximating the travel time function by a Taylor series and only using the first term. The residual can now be written:

ri = ((T/(xi) * (x + ((T/(yi) * (y + ((T/(zi) * (z + (t			(13)

In matrix form we can write this as

r = G * X,									(14)

where r is the residual vector, G the matrix of partial derivatives (with 1 in the last column corresponding to the source time correction term) and X is the unknown correction vector in location and origin time.

This is a set of linear equations with 4 unknowns (corrections to hypocenter and origin time), and there is one equation for each observed phase time. Normally there would be many more equations than unknowns (e.g., 4 stations with 3 phases each would give 12 equations). The best solution to Eq. (13) or Eq. (14) is usually obtained with standard least squares techniques. The original trial solution is then corrected with the results of Eq. (13) or Eq. (14) and this new solution can then be used as trial solution for a next iteration. This iteration process can be continued until a predefined breakpoint is reached. Breakpoint conditions can be either a minimum residuum r, a last iteration gives smaller hypocentral parameter changes than a predefined limit, or just the total number of iterations. This inversion method was first invented and applied by Geiger (1910) and is called the Geiger method of earthquake location. The iterative process usually converges rapidly unless the data are badly configured or the initial guess is very far away from the mathematically best solution (see later). However, it also happens that the solution converges to a local minimum and this would be hard to detect in the output unless the residuals are very bad. A test with a grid search program could tell if the minimum is local or tests could be made with several start locations.

So far we have only dealt with observations in terms of arrival times. Many 3-component stations and arrays now routinely report backazimuth of arrival (. It is then possible to locate events with only one station and P- and S-times (see Fig. 1). However, the depth must be fixed. If one or several backazimuth observations are available, they can be used together with the arrival time observations in the inversion and the additional equations for the backazimuth residual are

ri( = (((/(xi) * (x  + (((/(yi) * (y					(15)

Equations of this type are then added to the Eq. (13) or Eq. (14). The (x and (y in Eq. (15) are the same as for Eq. (13), however the residuals are now in degrees. In order to make an overall RMS, the degrees must be ‘converted to seconds’ in terms of scaling. For example, in the location program Hypocenter (Lienert and Havskov, 1995), a 10 deg backazimuth residual was optionally made equivalent to 1 s travel time residual. Using e.g., 20 deg as equivalent to 1 s would lower the weight of the backazimuth observations. Schweitzer (2001) used in the location program HYPOSAT a different approach. In this program the measured (or assumed) observation errors of the input parameters are used to weight individually the different lines of the equation system (13) or (14) before inverting it. Thereby, more uncertain observations will contribute much less to the solution than well-constrained ones and all equations become non-dimensional.

Arrays (see Chapter 9) or single stations (see Eq. (3)) cannot only measure the backazimuth of a seismic phase but also its ray parameter (or apparent velocity). Consequently, the equation system (13) or (14) to be solved for locating an event, can also be extended by utilizing such observed ray parameters p (or apparent velocities) as defining data. In this case we have can write

rip = ((p/(xi) * (x + ((p/(yi) * (y + ((p/(zi) * (z				(16)

Eq. (16) is independent from the source time and the partial derivatives are often very small. However, in some cases, in particular if an event is observed with only one seismic array, the observed ray parameter will give additional constrain for the event location.

Eqs. (13) and (14) are written without discussing whether working with a flat Earth or a spherical Earth. However, the principle is exactly the same and using a flat-Earth transformation (e.g., Müller, 1977) any radially symmetric Earth model can be transformed in a flat model. The travel times and partial derivatives are often calculated by interpolating in tables and in principle it is possible to use any Earth model including 2D and 3D models to calculate theoretical travel times. In practice, 1D models are mostly used, since 2D and 3D models are normally not well enough known and the travel-time computations are much more time consuming. For local seismology, it is a common practice to specify a 1D crustal model and calculate arrival times for each ray while for global models; an interpolation in travel-time tables such as IASPEI91 is the most common. However, as Kennett and Engdahl (1991) pointed out, the preferred and much more precise method for obtaining travel times from the IASP91 model or other 1D global Earth models (see Data Sheet DS 2.1) is to apply the tau-p method developed by Buland and Chapman (1983). To calculate own travel-time tables for local or global Earth models, the computer program LAUFZE can be downloaded from ftp://ftp.norsar.no/pub/outgoing/ johannes/lauf/. It allows calculating travel times for many different seismic phases and an arbitrary horizontally layered model with any combination of layers with constant velocities, gradients, or first-order discontinuities.

3.2.3	Example of location in a homogeneous model

The simplest case for earthquake location is a homogeneous medium. The travel times can be calculated as

,				(17)

where v is the velocity. The partial derivatives can be estimated from Eq. (17) and e.g., for x, the derivative is

.			(18)

Similar expressions can be made for y and z. Table 1 gives an example of locating an earthquake with 10 stations in a model with constant velocity (from Stein, 1991). The stations are from 11 to 50 km from the hypocenter. The earthquake has an origin time of 0 s at the point (0, 0, 10) km. The starting location is at (3, 4, 20) km at 2 s. The exact travel times were calculated using a velocity of 5 km/s and the iterations were done as indicated above. At the initial guess, the sum of the squared residuals were 92.4 s2, after the first iteration it was reduced to 0.6 s2 and already at the second iteration, the ‘correct’ solution was obtained. This is hardly surprising, since the data had no errors. We shall later see how this works in the presence of errors.

Table 1 Inversion of error free data. Hypocenter is the correct location, Start is the start location, and the location is shown for the two following iterations. Units for x, y and z are (km(, for t0 (s( and for the misfit e according to Eq. (11) (s2(.

|  | Hypocenter | Start | 1. Iteration | 2. Iteration |
| --- | --- | --- | --- | --- |
| X | 0.0 | 3.0 | -0.5 | 0.0 |
| Y | 0.0 | 4.0 | -0.6 | 0.0 |
| Z | 10.0 | 20.0 | 10.1 | 10.0 |
| t0 | 0.0 | 2.0 | 0.2 | 0.0 |
| e |  | 94.2 | 0.6 | 0.0 |
| RMS |  | 3.1 | 0.25 | 0.0 |

    - Advanced methods

The problem of locating seismic events has recently experienced a lot of attention and new procedures have been developed such as the double-difference earthquake location algorithm (Waldhauser and Ellsworth, 2000), a novel global differential evolution algorithm (Ružek and Kvasnička (2001), a probabilistic approach to earthquake location in 3D and layered models by Lomax et al. (2000) as well as advanced grid search procedures to be applied in highly heterogeneous media (Lomax et al., 2001). Recent advances in travel-time calculations for three-dimensional structures complements this method (e.g., Thurber and Kissling, 2000). Several of these and more most recent developments are summarized in a monograph edited by Thurber and Rabinowitz (2000), including also advances in global seismic event location (Thurber and Engdahl, 2000) and in a special volume about event location in context with the special requirements for monitoring the CTBT (Ringdal and Kennett, 2001). An example how much the accuracy of location within earthquake clusters can be improved by applying the above mentioned double-difference earthquake location algorithm is given in Figure 5.

Figure 5  Examples of improving the ABCE locations for earthquake clusters (red dots) from regional networks of seismic stations (triangles) in China by relocating the events with the double-difference location algorithm (courtesy of Paul G. Richards).

##### Location errors

4.1	Error quantification and statistics

Since earthquakes are located with arrival times that contain observational errors and the travel times are calculated assuming we know the model, all hypocenters will have errors. Contouring the grid search RMS (Figure 4) gives an indication of the uncertainty of the epicenter. Likewise it would be possible to make 3D contours to get an indication of the 3D uncertainty. The question is now how to quantify this measure. The RMS of the final solution is very often used as a criterion for ‘goodness of fit’. Although it can be an indication, RMS depends on the number of stations and does not in itself give any indication of errors and RMS is not reported by e.g., PDE and ISC.

From Figure 4 it is seen that the contours of equal RMS are not circles. We can calculate contours within which there is a 67 % probability (or any other desired probability) of finding the epicenter (see below). We call this the error ellipse. This is the way hypocenter errors normally are represented. It is therefore not sufficient to give one number for the hypocenter error since it varies spatially. Standard catalogs from PDE and ISC give the errors in latitude, longitude and depth, however, that can also be very misleading unless the error ellipse has the minor and major axis NS or EW. In the example in Figure 4, this is not the case. Thus the only proper way to report error is to give the full specification of the error ellipsoid.

Before going into a slightly more formal discussion of errors, let us try to get a feeling what elements affect the shape and size of the epicentral error ellipse. If we have no arrival time errors, there are no epicenter errors so the magnitude of the error (size of error ellipse) must be related to the arrival time uncertainties. If we assume that all arrival time reading errors are equal, only the size and not the shape of the error ellipse can be affected. So what would we expect to give the shape of the error ellipse? Figure 4 is an example of an elongated network with the epicenter off to one side. It is clear that in the NE direction, there is a good control of the epicenter since S-P times control the distances in this direction due to the elongation of the network. In the NW direction, the control is poor because of the small aperture of the network in this direction. We would therefore expect an error ellipse with the major axis NW as observed. Another way of understanding why the error is larger in NW than in NE direction is to look at Eq. (12). The partial derivatives (T/(x will be much smaller then (T/(y so the (y-terms will have larger weight then the (x-terms in the equations (strictly speaking the partial derivatives with respect to NW and NE). Consequently, errors in arrival times will affect (x more than (y. Note, that if backazimuth observations were available for any of the stations far North or South of the event, this would drastically reduce the error estimate in the EW direction since ((/(x is large while ((/(y is nearly zero.

Another geometry of the stations would give another shape of the error ellipse. It is thus possible for any network to predict the shape and orientation of the error ellipses, and given an arrival error, also the size of the ellipse for any desired epicenter location. This could e.g., be used to predict how a change in network configuration would affect earthquake locations at a given site.

In all these discussions, it has been assumed that the errors have Gaussian distribution and that there are no systematic errors like clock error. It is also assumed that there are no errors in the theoretical travel times, backazimuths, or ray parameter calculations due to unknown structures. This is of course not true in real life, however error calculations become too difficult if we do not assume a simple error distribution and that all stations have the same arrival time error.

The previous discussion gave a qualitative description of the errors. We will now show how to calculate the actual hypocentral errors from the errors in the arrival times and the network configuration. The most common approach to earthquake location is based the least squares inversion and a Gaussian distribution of the arrival time errors in which case the statistics is well understood and we can use the Chi-Square probability density distribution to calculate errors. For a particular earthquake location, (2 can be calculated as:

,						(19)

where ( is the assumed same standard deviation of any one of the residuals and n is the number of observations. We can now look in standard statistical tables (extract in Table 2) to find the expected value of (2 within a given probability. As it can be seen from the table, within 5% probability, (2 is approximately the number of degrees of freedom (ndf), which in our case is n-4.

Table 2  The percentage points of the (2 distribution for different number of degrees of freedom (ndf)

| ndf | (2 (95%) | (2 (50%) | (2 (5%) |
| --- | --- | --- | --- |
| 5 | 1.1 | 4.4 | 11.1 |
| 10 | 3.9 | 9.3 | 18.3 |
| 20 | 10.9 | 19.3 | 31.4 |
| 50 | 34.8 | 49.3 | 67.5 |
| 100 | 77.9 | 99.3 | 124.3 |

If e.g., an event is located with 24 stations (ndf=20), there is only a 5% chance that (2 will exceed 31.4. The value of (2 will grow as we move away from the best fitting epicenter and in the example above, the contour within which (2 is less than 31.4 will show the error ellipse within which there is 95 % chance of finding the epicenter. In practice, errors are mostly reported within 67 % probability.

The errors in the hypocenter and origin time can also formally be defined with the variance – covariance matrix (X2 of the hypocentral parameters. This matrix is defined as

.						(20)

The diagonal elements are variances of the location parameters x, y, z and t0 while the off diagonal elements give the coupling between the errors in the different hypocentral parameters. For more details, see e.g., Stein (1991). The nice property about (X2 is that it is simple to calculate:

(X2 = (2 * (GTG)-1,								(21)

where (2 is the variance of the arrival times multiplied with the identity matrix and GT is G transposed. The standard deviations of the hypocentral parameters are thus given by the square root of the diagonal elements and these are the usual errors reported. So how can we use the off diagonal elements? Since (X2 is a symmetric matrix, a diagonal matrix in a coordinate system, which is rotated relatively to the reference system, can represent it. We now only have the errors in the hypocentral parameters, and the error ellipse simply have semi axes (xx, (yy, and (zz . The main interpretation of the off diagonal elements is thus that they define the orientation and shape of the error ellipse. A complete definition therefore requires 6 elements. Eqs. (20) and (21) also show, as earlier stated intuitively, that the shape and orientation of the error ellipse only depends on the geometry of the network and the crustal structure while the standard deviation of the observations is a scaling factor.

The critical variable in the error analysis is thus the arrival-time variances (2. This value is usually larger than would be expected from timing and picking errors alone, however it might vary from case to case. Setting a fixed value for a given data set could result in unrealistic error calculations. Most location programs will therefore estimate ( from the residuals of the best fitting hypocenter:

.						(22)

Division by ndf rather then by n compensates for the improvement in fit resulting from the use of the arrival times from the data. However, this only partly works and some programs allow setting an a priori value, which is only used if the number of observations is small. For small networks this can be a critical parameter.

Recently, some studies (e.g., Di Giovambattista and Barba, 1997; Parolai et al., 2001) showed, both for regional and local seismic networks, that the error estimates ERH (in horizontal) and ERZ (in vertical direction), as given by routine location programs (e.g., in Hypoellipse) can not be considered as a conservative estimate of the true location error and might encourage investigators to unjustified tectonic conclusions (see also Figures 12 and 13).

4.2	Example of error calculation

We can use the previous error free example (Table 1) and add some errors (from Stein, 1991). We add Gaussian errors with a mean of zero and a standard deviation of 0.1 s to the arrival times. Now the data are inconsistent and cannot fit exactly. As it can be seen from the results in Table 3, the inversion now requires 3 iterations (2 before) before the locations do not change anymore. The final location is not exactly the location used to generate the arrival times and the deviation from the correct solution is 0.2, 0.4, and 2.2 km for x, y, and z respectively and 0.2 s for origin time. This gives an indication of the location errors.

Table 3  Inversion of arrival times with a 0.1 s standard error. Hypocenter is the correct location, Start is the start location, and the locations are shown after the three following iterations. e is the misfit according to Eq. (11).

|  | Hypocenter | Start | 1. Iteration | 2. Iteration | 3. Iteration |
| --- | --- | --- | --- | --- | --- |
| x [km] | 0.0 | 3.0 | -0.2 | 0.2 | 0.2 |
| y [km] | 0.0 | 4.0 | -0.9 | -0.4 | -0.4 |
| z [km] | 10.0 | 20.0 | 12.2 | 12.2 | 12.2 |
| t0 [s] | 0.0 | 2.0 | 0.0 | -0.2 | -0.2 |
| e (s2( |  | 93.7 | 0.33 | 0.04 | 0.04 |
| RMS [s] |  | 3.1 | 0.25 | 0.06 | 0.06 |

It is now interesting to compare to what is obtained with the formal error calculation. Table 4 gives the variance – covariance matrix. Taking the square root of the diagonal elements we get a standard deviation of x, y, z and t0 of 0.3, 0.3 and 1.1 km and 0.1 s respectively. This is close to the ‘true’ error so the solution is quite acceptable. Also note that the RMS is close to the standard error.

Table 4  Variance – covariance matrix for the example in Table 3.

|  | x | Y | Z | t |
| --- | --- | --- | --- | --- |
| x | 0.06 | 0.01 | 0.01 | 0.00 |
| y | 0.01 | 0.08 | -0.13 | 0.01 |
| z | 0.01 | -0.13 | 1.16 | -0.08 |
| t | 0.00 | 0.01 | -0.08 | 0.0 |

The variance – covariance matrix shows some interesting features. As seen from the dialog elements of the variance – covariance matrix, the error is much larger in the depth estimate than in x and y. This clearly reflects that the depth is less well constrained than the epicenter which is quite common unless there are stations very close to the epicenter and thus |(d-()| / ( >> 1. We have for simplicity calculated the standard deviations from the diagonal terms, however since the off diagonal terms are not zero, the true errors are larger. In this example it can be shown that the semimajor and semiminor axis of the error ellipse have lengths of 0.29 and 0.24 km respectively and the semimajor axis trends N22(E so the difference from the original diagonal terms is small.

The zt term, the covariance between depth and origin time, is negative, indicating a negative trade-off between the focal depth and the origin time; an earlier source time can be compensated by a larger source depth and vice versa. This is commonly observed in practice and is more prone to happen if only first P-phase arrivals are used such that there is no strong limitation of the source depth by P-times in different distances.

Error calculation is a fine art, there are endless variations on how it is done and different location programs will usually give different results.

##### 5	Relative location methods

5.1	Master event technique

The relative location between events within a certain region can often be made with a much greater accuracy than the absolute location of any of the events. This is the case when velocity variations outside the local region are the major cause of the travel-time residuals such that residuals measured at distant stations will be very similar for all of the local events. Usually, the events in the local area are relocated relative to one particularly well-located event, which is then called the master event. It should be clear that the Master Event Technique could only be used when the distance to the stations is much larger than the distance between the events.

Most location programs can be used for a master event location. For this travel-time anomalies outside the source region are assumed to cause all individual station residuals after the location of the master event. By using these station residuals as station corrections, the location of the remaining events will be made relative to the master event since all relative changes in arrival times are now entirely due to changes in location within the source region. It is obvious that only stations and phases for which observations are available for the master event can be used for the remaining events. Ideally, the same stations and phases should be used for all events.

5.2	Joint hypocenter location

In the Master Event Technique, it was assumed that true structure dependent residuals could be obtained absolutely correct from the master event, however other errors could be present in the readings for the master event. A better way is to determine the most precise station residuals using the whole data set. This is what Joint Hypocenter Determination (JHD) is about. Instead of determining one hypocenter and origin time, we will jointly determine m hypocenters and origin times, and n station corrections. This is done by adding the station residuals (tis to Eq. (13) and writing the equations for all m earthquakes (index j):

rij = ((T/(xij) * (x + ((T/(yij) * (y + ((T/(zij) * (x + (tis + (tj.		    (23)

The first who proposed the JHD method was Douglas (1967). Since the matrix G of Eq. (14) is now much larger than the 4 x 4 matrix for a single event location, efficient inversion schemes must be used. If we use e.g., 20 stations with 2 phases each for 10 events, there will be 20 *10 *2 = 400 equations and 80 unknowns (10 hypocenters and origin times, and 20 station residuals).

The relative locations obtained by the Master Event Technique or the JHD are usually more reliable than individually estimated relative locations. However, only if we have the absolute location of one of the events (e.g., a known explosion), we will be able to convert the relative locations of a Master Event algorithm to absolute locations. While for JHD, “absolute” locations are obtained for all events if the assumed velocity model is correct. Accurate relative locations are useful to study e.g., the structure of a subduction zone or the geometry of an aftershocks area, which might indicate the orientation and geometry of the fault. Recently, Pujol (2000) gives a very detailed outline of the method and its application to data from local seismic networks. Figure 5 shows an example for increased location accuracy after applying JHD.

Figure 6  Comparison of earthquake locations using the normal procedure at ISC (left) and JHD relocations (right). The events are located in the Kurile subduction zone along the rupture zones of large thrust events in 1963 and 1958. The vertical cross sections shown traverse the thrust zone from left to right. Note that the JHD solutions reduce the scatter and make it possible to define a dipping plane (from Schwartz et al., 1989).

# 6	Practical consideration in earthquake locations

This section is intended to give some practical hints on earthquake location. The section does not refer to any particular location program, but most of the parameters discussed can be used with the Hypocenter program (Lienert and Havskov, 1995) or with HYPOSAT (Schweitzer, 2001).

6.1	Phases

The most unambiguous phase to pick is usually P and P is the main phase used in most teleseismic locations. For local earthquakes, usually S-phases are also used. Using phases with different velocities and slowness has the effect of better constraining the distances and there is then less trade-off between depth and origin time or epicenter location and origin time if the epicenter is outside the network. The focal depth is best controlled (with no trade-off between depth and origin time) when phases are included in the location procedure which have different sign of the partial derivative (T/(z in Eq. (13) such as for very locally observed direct up-going Pg (positive) and Pn (negative) (see section 6.3 Hypocentral depth and Figure 9). In general, it is thus an advantage to use as many different phases as possible under the assumption that they are correctly identified. Recently Schöffel and Das (1999) gave a striking example (see Figure 7). But one very wrong phase can throw off an otherwise well constrained solution. This highlights the crucial importance of the capability of the observatory personal to recognize and report such phases already during their routine seismogram analysis.

Figure 7  Examples of significant improvement of hypocenter location for teleseismic events by including secondary phases. Left: hypocenter locations using only P-phases; middle: by including S-phases; right: by including also depth phases and core reflections with different sign of (T/(z (from Schöffel and Das, 1999).

Engdahl et al (1998) used the entire ISC database to relocated more than 100.000 seismic events. They used not only a new scheme to associate properly secondary phases but they also systematically searched for pwP onsets in case of subduction-zone events to get better depth estimates and they used a modern global Earth model (AK135) to avoid the known problems with the Jeffreys-Bullen tables. With all these changes the authors reached a far more consistent distribution (in particular for subduction zones) and sharper picture of global seismicity.

The majority of location programs for local earthquakes only use first arrivals (e.g., HYPO71, Lee and Lahr, 1975). This is good enough for many cases. In some distance ranges, Pn is the first arrival, and it usually has a small amplitude. This means that the corresponding Sn phase, which is then automatically used by the program, might have also a very small amplitude and is not recognized while actually the phase read is Sg or Lg instead. Since the program automatically assumes a first arrival, a wrong travel time curve is used for the observed phase, resulting in a systematic location error. This error is amplified by the fact that the S-phase, due to its low velocity, has a larger influence on the location than the P-phase. It is therefore important to use location programs where all crustal phases can be specified.

Schweitzer (2001) developed an enhanced routine to locate both local/regional and teleseismic events, called HYPOSAT. The program runs with global Earth models and user defined horizontally layered local or regional models. It provides best possible hypocenter estimates of seismic sources by using besides the usual input parameters such as arrival times of first and later onsets (complemented by backazimuth and ray parameters in case of array data or polarization analyses) also travel-time differences between the various observed phases. If S observations are also available, preliminary origin times are estimated by using the Wadati approach (see Figure 3) and a starting epicenter with a priori uncertainties by calculating the intersection of all backazimuth observations. Relocating events with real data Schweitzer could show that HYPOSAT solutions have the smallest errors when besides the absolute onset times also the travel-time differences of all available primary and secondary phase readings are taken into account. The most advanced version of HYPOSAT can be found at ftp://ftp.norsar.no/pub/outgoing/johannes/hyposat/ and a program description is annexed in PD 11.1.

6.2	Starting location

Iterative location programs commonly start at a point near the station recording the first arrival. This is good enough for most cases, particularly when the station coverage is good and the epicenter is near or within the network. However, this can also lead to problems when using least squares techniques, which converge slowly or sometimes not at all for events outside the limits of a regional network (Buland, 1976). Another possibility is that the solution converges to a local minimum, which might be far from the correct solution. For small-elongated networks, two potential solutions may exist at equal distance from the long axis. A starting location close to the first arrival station can then bias the final solution to the corresponding side of such a network. Although this bias usually is on the correct side, any systematic error in the first-arrival station’s time can have a disproportionately large effect on the final location. Thus in many cases, it is desirable to use a better start location than the nearest station. There are several possibilities:

- In many cases the analyst knows by experience the approximate location and can then manually give a start location. Most programs have this option.

- Similar phases at different stations can be used to determine the apparent velocity and backazimuth of a plane wave using linear regression on the arrival times with respect to the horizontal station coordinates. With the apparent velocity and/or S-P times, an estimate of the start location can be made. This method is particularly useful when locating events far away from the network (regionally or globally).

- Backazimuth information is frequently available from 3-component stations or seismic arrays and can be used as under b.

- If backazimuth observations are available from different stations, a starting epicenter can be determined by calculating the intersection of all backazimuth observations.

- S-P and the circle method can be used with pairs of stations to get an initial location.

- The Wadati approach can be used to determine a starting source time.

The starting depth is usually a fixed parameter and set to the most likely depth for the region. For local earthquakes usually the depth range 10-20 km is used, while for distant events, the starting depth is often set to 33 km. If depth phases like e.g., pP are available for distant events, these phases can be used to set or fix the depth (see next section).

6.3	Hypocentral depth

The hypocentral depth is the most difficult parameter to determine due to the fact that the travel-time derivative with respect to depth changes very slowly as function of depth (see Figure 8) unless the station is very close to the epicenter. In other words, the depth can be moved up and down without changing much the travel time. Figure 8 shows a shallow (ray 1) and a deeper event (ray 2). It is clear that the travel-time derivative with respect to depth is nearly zero for ray 1 and but not for ray 2. In this example, it would thus be possible to get an accurate depth estimate for the deeper event but not for the shallower one. Unfortunately, at larger distances from the source, most rays are more like ray 1 than like ray 2 and locations are therefore often made with a fixed ‘normal’ start depth. Only after a reliable epicenter is obtained the program will try to iterate for the depth. Another possibility is to locate the event with several starting depths and then using the depth that gives the best fit to the data. Although one depth will give a best fit to all data, the depth estimate might still be very uncertain and the error estimate must be checked.

Figure 8  The depth – distance trade off in the determination of focal depth.

For teleseismic events, the best way to improve the depth determination is to include readings from the so-called depth phases (e.g., Gutenberg and Richter, 1936 and 1937; Engdahl et al., 1998) such as pP, pwP (reflection from the ocean free surface), sP, sS or similar but also reflections from the Earth´s core like PcP, ScP or ScS (see Figure 7). The travel-time differences (i.e., depth phase – direct phase) as pP-P, sP-P, sS-S, and pS-S are quite constant over large range of epicentral distances for a given depth so that the depth can be determined nearly independently of the epicenter distance. Another way of getting a reliable depth estimate for teleseismic locations is to have both near and far stations available. In particular, event observations from local and regional stations and with PKP observations had been used together for this purpose. However, this is unfortunately for many source regions not possible.

For local events, a rule of thumb is that at least several near stations should be not further away than 2 times the depth in order to get a reliable estimate (Figure 8). This is very often not possible, particularly for regional events. At distance larger than 2 ( depth, the depth depending partial derivative changes very little with depth if the first arriving phase is the more or less horizontally propagating Pg. But at distances where the critically refracted (so-called head-waves) Pb or Pn arrive, there is again some sensitivity to depth due to the steeply down going rays of Pb or Pn (Figure 9) and because of the different sign of the partial derivatives of their travel times with depth, which is negative, as compared to Pg, which is positive. So, if stations are available at distances with both direct and refracted rays as first arrivals, reasonably reliable solutions might be obtained. An even better solution is when both Pg and Pn are available at the same station and the location capability could be similar to using P and pP for teleseismic events. The problem is that it might be difficult to identify correctly secondary P-phases and a wrong identification might make matters worse.

Figure 9  Example of both Pg and Pn rays in the a single layer crustal model.

The depth estimate using a layered crustal model remains problematic even with a mix of phases. Checking catalogs with local earthquakes, it will often be noted that there is a clustering of hypocenters at layer boundaries. This is caused by the discontinuities in the travel-time curves of the direct phase Pg as a function of depth at layer boundaries; see Figure 8 for an example. The Pg travel time suddenly decreases when the hypocenter crosses a boundary (here Moho) since a larger part of the ray suddenly is in a higher velocity layer, while the Pn travel time continuously decreases as the depth increases as long as the event is still within the crust. This gives rise to the discontinuities in the Pg-Pn travel-time curve. So one Pn-Pg travel-time difference is not enough to ensure a reliable depth estimate, several such phase arrivals must be available.

Figure 10  Ray paths of Pg and Pn phases in a two-layer crustal model (left). On the right side the travel-time curve of Pg-Pn as a function of depth is sketched.

Even when several Pg and Pn phases are available, depth estimates still remains a problems at regional distances due to the uncertainty in the crustal models. Since the depth estimates are critically dependent on the accurate calculation of Pg and Pn travel times, small uncertainties in the model can quickly throw off the depth estimate.

Many location programs give the RMS of the travel-time residuals in a grid around the calculated hypocenter. This, in addition to the error estimates, gives an idea about the accuracy and a local minimum might be found in this way. A more direct way of estimating the quality of the depth estimate is to calculate the RMS as a function of depth in order to check if a local minimum has been reached. This is particularly relevant for crustal earthquakes at shallow depth and can also be used as a complementary tool for better discriminating between quarry blasts and earthquakes.

6.4	Outliers and weighting schemes

The largest residuals have disproportionally large influence on the fit of the arrival times due to the commonly used least squares fit. Most location programs will have some kind of residual weighting scheme in which observations with large residuals are given lower or even no weight. Bisquare weighting is often used for teleseismic events (Anderson, 1982). The residual weighting works very well if the residuals are not extreme since the residual weighting can only be used after a few iterations so that the residuals are close to the final ones. Individual large residuals can often lead to completely wrong solutions, even when 90 % of the data are good, residual weighting will not help in these cases. Some programs will try to scan the data for gross errors (like minute errors) before starting the iterative procedure. If an event has large residuals, try to look for obvious outliers. A Wadati diagram can often help in spotting bad readings for local earthquakes (see Figure 3).

The arrival-time observations will by default always have different weights in the inversion. A simple case is that S-waves may have larger weights than P-waves due to their lower velocities. An extreme case is the T-wave (a guided waves in the ocean), which with its low velocity (1.5 km/s) can completely dominate the solution. Considering, that the accuracy of the picks is probably best for the P-waves, therefore it should be natural, that P-arrivals should have more importance than S-arrivals in the location. However, the default parameter setting in most location programs is to leave the original weights unless the user actively changes them. It is normally possible to give ‘a priori’ for all S-phases a lower weight and in addition, all phases can be given individual weights, including being totally weighted out.

When working with local earthquakes, the nearest stations will usually provide the most accurate information due to the clarity of the phases. In addition, uncertainty in the local model has less influence on the results at short distances than at larger distances; this is particularly true for the depth estimate. It is therefore desirable to put more weight on data from near stations than on those from distant stations and this is usually done by using a distance weighting function of

,							(24)

where ( is the epicentral distance, xnear is the distance to which full weight is used and xfar is the distance where the weight is set to zero (or reduced). The constants xnear and xfar are adjusted to fit the size of the network; xnear should be about the diameter of the network, and xfar about twice xnear. For a dense network, xnear and xfar might be made even smaller to more accurate solutions.

  - Ellipticity of the Earth

Until now we only assumed that the model used for calculating distances or travel times is either for local or regional events a flat model or for teleseismic events a standard spherical model of the Earth. However, the Earth is neither a sphere nor a flat disk but an ellipsoid symmetrical to its rotation axis. It was Gutenberg and Richter (1933) who first pointed out that the difference between a sphere and an ellipsoid must be taken in account when calculating epicentral distances and consequently also the travel times of seismic phases. Therefore, they proposed the usage of geocentric coordinates instead of geographic coordinates to calculate distances and angles on the Earth. Because of the axially symmetrical figure of the Earth, the geocentric longitude is identical to the geographic longitude. To convert a geographic latitude latg into a geocentric latitude latc one can use the following formula:

.		(25)

With this formula all station latitudes have to be converted before an event location and after the inversion, the resulting geocentric event latitude has to be converted back by applying the inverse equation

.		(26)

With this procedure all angle calculations related to an event location are done for a sphere. The calculated distances are measured in degrees and to convert them in km, one has to use the local Earth radius Rloc:

.			(27)

This value has then to be applied for converting a distance D measured in degrees into a distance measured in km, or vice versa:

or			(28)

All standard Earth models are spherically symmetrical Earth with a mean radius of 6371 km. Therefore the standard tables also contain travel times calculated for a sphere. Bullen (1937, 1938, 1939) was the first, who calculated latitude depending travel-time corrections (ellipticity corrections) to be used together with travel-time tables for a spherical Earth. Later work on this topic was done by Dziewonski and Gilbert (1976) and Dornboos (1988). Kennett and Gudmundsson (1996) published the most recent set of ellipticity corrections for a large number of seismic phases.

In conclusion: to get the theoretical travel time for an event in teleseismic or regional distance, one has to calculate the geocentric epicentral distance, then one has to use travel-time tables as calculated for a spherical Earth model, and finally one has to apply the latitude (event and station!) depending ellipticity correction. Most location routines do automatically apply the described methods and formulas but it is important to check this in detail and eventually to change a location program.

6.6	Importance of the model

In this context the importance of the model assumptions underlying the location procedure have to be emphasized. Many studies showed (e.g., Kissling, 1988) that accuracy of locating hypocenters can be improved by using a well-constrained minimum 1D velocity model with station corrections is better than using a regional 1D model. However, Spallarossa et al. (2001) recently showed, that in strongly heterogeneous local areas even a 1D model with station corrections does not significantly improve the accuracy of the location parameters. High-precision location can in such case be achieved only be using a 3D model. This is particularly true for locating earthquakes in volcanic areas (see Lomax et al., 2001).

Smith and Ekström (1996) investigated the improvement of teleseismic event locations by using a recent three-dimensional Earth models. They came to the conclusion that it “... offers improvement in event locations over all three 1D models with, or without, station corrections.” For the explosion events, the average mislocation distance is reduced by approximately 40 %; for the earthquakes, the improvements are smaller. Corrections for crustal thickness beneath source and receiver are found to be of similar magnitude to the mantle corrections, but use of station corrections together with the 3D mantle model provide the best locations. Also Chen and Willemann (2001) carried out a global test of seismic event locations using three-dimensional Earth models. Although achieved by using a 3D model a more tightly clustering of earthquakes in subduction zones than by using depth from the ISC Bulletin based on 1D model calculations, they concluded that the clustering was not as tightly as for depths computed by Engdahl at al. (1998) who used depth phases as well as direct phases. Thus, even using the best available global 3D models can not compensate for the non-use of depth phases and core reflections in teleseismic hypocenter location (see Figure 7).

A case example for improved location of local events is given in Figures 11 and 12. The upper panel in Figure 11 shows the initial locations for aftershocks of the Cariaco earthquake (Ms = 6.8) on July 9, 1997 in NE of Venezuela based an averaged 1D crustal velocity model. The mean location error (i.e., the calculated precision with respect to the assumed model) was about 900 m. On the average, the aftershocks occurred about 2 to 3 km north of the surface fault trace. A detailed tomographic study revealed lateral velocity contrasts of up to 20 % with higher velocities towards the north of the El Pilar fault. Relocating the events with the 3D velocity model the epicenters were systematically shifted southward by about 2 km and now align in their majority rather well with fault traces mapped before the earthquake as well as with newly ruptured fault traces. Also in the cross sections the data scatter was clearly reduced so that closely spaced outcropping surface faults could be traced down to a depth of more than 10 km. This results hints to the fact that in the presence of lateral velocity inhomogeneities epicenter locations are systematically displaced in the direction of higher velocities. We will look into this problem more closely in section 7.

Figure 11  Epicentral distribution of aftershocks of the Cariaco earthquake (Ms=6.8) on July 9, 1997 in NE of Venezuela. Top: results from HYPO71 based on a one-dimensional velocity-depth distribution. Bottom: Relocation of the aftershocks on the basis of a three-dimensional model derived from a tomographic study of the aftershock region (courtesy of M. Baumbach, H. Grosser and A. Rietbrock).

Figure 12  3-D distribution of the P-wave velocity in the focal region of the 1997 Cariaco earthquake as derived from a tomographic study. The horizontal section shows the velocity distribution in the layer between 2 km and 4 km depth. Red and blue dots mark the epicenters of the aftershocks. The red ones were chosen because of their suitability for the tomograpy. The six vertical cross sections show the depths distribution of the aftershocks (green dots) together with the deviations of the P-wave velocity from the average reference model. The depth range and the lateral changes of fault dip are obvious (courtesy of M. Baumbach, H. Grosser and A. Rietbrock).

#### 7	Internal and external (real) accuracy of locations

For decades the international data centers have located earthquakes world-wide by means of the 1D Jeffreys and Bullen (1940, 1948, 1958, 1967, and 1970) travel-time tables without external control of the accuracy of such solutions by checking them independent and similarly strong events of exactly known position and origin time. Therefore, the question remained open for a long time whether these calculated location errors were real or just the minimized average errors for the best fitting solutions to the observed data based on the various model assumptions made with respect to the validity of the velocity model, the non-correlation of the various parameters to be determined and the Gaussian distribution of the model and data reading errors involved. If the latter was the case then the calculated errors were not measure of the real accuracy of the calculated location and origin time but rather a measure of the internal precision of fitting the data to the model assumptions.

In order to investigate this in more detail, Bormann (1972) looked into the travel-time errors reported by the international data centers for the German seismological observatory Moxa (MOX) for earthquakes in different regions of the world. As and example, he got for the same data set of events from the Kurile Islands the mean residual((tp = + 0.16 s and a standard deviation ( = ( 0.65 s when referring the MOX onset-time readings to the locations published by the U.S. Coastal and Geodetic Survey (USCGS, World Data Center A, WDC A) and ((tp = + 0.35 s with ( = ( 1.1 s when referred to the locations published by the Academy of Sciences of the Soviet Union (ANUSSR, World Data Center B, WDC B) which used the same J-B travel-time model as USCGS. Thus, the travel-time (or onset-time reading) errors calculated by the data centers for seismic stations are not real errors of these stations or their readings but depend on the number and distribution of stations used by these centers in their location procedure. And these were rather different for WDC A and WDC B. While the USCGS used the data of a worldwide station network ANUSSR based its locations on the station network of the former Soviet Union and East European countries and these “looked at” events outside of Eurasia from a much narrower azimuth and distance range. But this is just equivalent to the above discussion related to Figure 4. The mean residuals calculated by these two centers for the considered region were not significantly different and not far from zero. Therefore, the question remained whether there were systematic biases in these solutions and if so, of what kind and how big they were.

From the 60's onwards testing of strong underground nuclear explosions (UNE) provided for the first time independent strong sources with precisely known coordinates and origin time which allowed to check the accuracy of calculated seismic source locations from global seismic observations. During the last years for many UNEs such information was released. However, for the LONGSHOT explosion on the Amchitka Islands, Aleutians, the source parameters were known since many years. For this event the residual of MOX was (tp = -4.6 s! This contrasted strongly with calculated residuals for Aleutian earthquakes. From 53 analyzed earthquakes in that region, no negative residual at MOX was larger than -0.8 s! Interestingly, the USGS had calculated for LONGSHOT a location 25 km NW of the true place (which explains -1 s travel-time error at MOX) and an origin time which was 3.5 s earlier then the real one (which accounts for the remaining -3.5 s!) (Sykes, 1966). The too early source time is a meanwhile well-understood artifact of the Jeffreys-Bullen tables, which generally give too long P-phase travel times. According to Fedotov and Slavina (1968) epicenters calculated by the WDC B from events in the Aleutians are generally displaced towards NW with respect to those of the WDC A. Consequently, with the same systematic tendency of shift, they deviated still more from the true locations of events in that area.

To get the best geographic coverage for each seismic event, the ISC waits with its event location about two years to collects as much as possible seismogram readings from all worldwide distributed seismological observatories.

What is the reason for this systematic mislocation, which usually remains unrecognized unless one locates strong independently controlled sources of exactly known source parameters and origin time? Figure 13 shows some hypothetical earthquakes at different depth on a vertically dipping fault. It separates two half-spaces with different wave propagation velocity v2 > v1. This is a realistic model for parts of the San Andreas Fault. The lateral velocity difference across the fault may be as large as 5 to 7 %. S1 and S2 may be two stations at the same hypocentral distances from the events. But because of v2 > v1 the onset time t2 at S2 is earlier (travel-time shorter) than for t1 at S1. Running now the location procedure with the common residual minimization on the assumption of a laterally homogeneous velocity model will result in hypocentral distances d2(h) < d1(h). Since the difference increases with depth, the hypocenters are not only offset from the real fault but seem to mark even a slightly inclined fault, which is not the case.

Figure 13  Illustration of the systematic mislocation of earthquakes along a fault with strong lateral velocity contrast. vo is the assumed model velocity with v2 > vo > v1.

From this hypothetical example we learn that localizations based on 1D velocity models in the presence of 2D or 3D velocity inhomogeneities will be systematically shifted in the direction of increasing velocities (or velocity gradients), the more so the less the station distribution controls the event from all azimuths. Precisely this was the cause for the larger systematic mislocation of WDC B as compared to WDC A. While the latter localizes events using data from a global network, the former used solely data from the former Soviet and East European territory, i.e., stations which view the Aleutian Islands only from a narrow azimuth range. The direction of systematic mislocation of both centers to the NW agrees with the NW directed subduction of the Pacific plate underneath the Aleutians. According to Jacob (1972) this cold lithospheric plate has 7 to 10% higher P-wave velocities than the surrounding mantle. A recent study by Lienert (1997) addresses also this problem of assessing the reliability of earthquake locations by using known nuclear tests.

### Acknowledgements

Part of text follows a similar description in Shearer (1999). Figures and ideas have also been taken from Stein (1991), Lay and Wallace (1995), Schöffel and Das (1999). Special thanks go to M. Baumbach, H. Grosser and A. Rietbrock for making Figures 11 and 12 available and to R. E. Engdahl for critical proof reading and valuable suggestions which helped to improve the text and to complement the references.

#### References

Anderson, K. R. (1982). Robust earthquake location using M-estimates, Phys. Earth. Plan. Inter 30, 119-130.

Bormann, P. (1972). A study of travel-time residuals with respect to the location of teleseismic events from body-wave records at Moxa station. Gerlands Beiträge zur Geophysik 81, 117-124.

Buland,R. (1976). The mechanics of locating earthquakes, Bull. Seism. Soc. Am. 66, 173-187.

Buland, R. and Chapman, C. H. (1983). The computation of seismic travel times. Bull. Seism. Soc. Am., 73. 1271-1303.

Bullen, K.E. (1937, 1938, 1939). The elliptcity correction to travel-times of P and S earthquake waves. Montl. Not. R. Astr. Soc., Geophys. Suppl. 4, 143-157, 158-164, 317-331, 332-337, 469-471.

Båth, M.(1979). Introduction to seismology, 428 pp., Birkhäuser Verlag. Basel.

Chen, Q.F. and Willemann, R. J. (2001). Global test of seismic event locations using three dimensional Earth models. Bull. Seis. Soc. Am. 91, 1704-1716.

Di Giovambattista, R. and Barba, S. (1997). An estimate of hypocenter location accuracy in a large network, possible implication for tectonic studies in Italy. Geophys. J. Int. 129, 124-132.

Dornboos, D.J. (1988). Asphericity and ellipticity corrections. In: Dornboos, D.J. (ed.). Seismological Algorithms. Academic Press, New York 1988, 17 + 469 pp.

Douglas, A. (1967). Joint hypocenter determination. Nature 215, 47-48.

Dziewosnki, A.M. and Gilbert, F. (1976). The effect of small, aspherical perturbations on travel times and a re-examination of the corrections for ellipticity. Geophys. J. R. Astr. Soc. 44, 7-17.

Engdahl, E.R., van der Hilst. R. and Buland, R. (1998), Global teleseismic earthquake relocation with improved travel times and procedures for depth determination, Bull. Seism. Soc. Am. 88, 722-743.

Fedotov, S.A. and Slavina, L.B. (1968). Estimate of the velocity of longitudinal waves in the upper mantle under the northwestern part of the Pacific Ocean and Kamchatka (in Russian). Izv. Akad. Nauk SSSR, Fizika Zemli 2, 8-31.

Geiger, L. (1910). Herdbestimmung bei Erdbeben aus den Ankunftszeiten. Nachrichten von der Königlichen Gesellschaft der Wissenschaften zu Göttingen, Mathematisch-Physikalische Klasse, 331-349. (1912 translated to English by F.W.L. Peebles and A.H. Corey: Probability method for the determination of earthquake epicenters from the arrival time only. Bulletin St. Louis University 8, 60-71).

Gomberg, J. S., Shedlock, K. M., and Roecker, W. W. (1990). The effect of S-wave arrivals times on the accuracy of hypocenter estimation. Bull. Seism. Soc. Am., 80, 6, 1605-1628.

Gutenberg, B. and Richter, C.F. (1933). Advantages of using geocentric latitude in calculating distances. Gerlands Beiträge zur Geophysik 40, 380-389.

Gutenberg, B. and C.F. Richter (1936). Materials for the study of deep-focus earthquakes. Bull. Seism. Soc. Am. 26, 341 – 390 (edition in French: Données relatives a l'étude des tremblements de terre a foyer profond. Publications du Bureau Central Séismologique International, Série A, Travaux Scientifiques 15, 1 - 70, 1937).

Gutenberg, B. and C.F. Richter (1937). Materials for the study of deep-focus earthquakes (second paper). Bull. Seism. Soc. Am. 27, 157 – 184 (partly edited in French: Données relatives a l'étude des tremblements de terre a foyer profond. Publications du Bureau Central Séismologique International, Série A, Travaux Scientifiques 15, 1 - 70, 1937).

Jacob, K.H. (1972). Global tectonic implications of anomalous seismic P travel-times from the nuclear explosion Longshot. J. Geophys. Res. 77, 14.

Jeffreys, H. and Bullen,K.E. (1940, 1948, 1958, 1967, and 1970). Seismological Tables, British Association for the Advancement of Science, Gray Milne Trust, London, 50 pp.

Kissling, E. (1988). Geotomography with local earthquake data. Rev. Geophys. 26, 659-698.

Kennett, B.L.N. (1991). IASPEI 1991 Seismological Tables. Australian National University, Research School of Earth Sciences, 167 pp.

Kennett, B.L.N., and Engdahl, E.R. (1991), Travel times for global earthquake location and phase identification, Geophys. J. Int. 105, 429-466.

Kennett, B.L.N., Engdahl, E.R., and Buland, R. (1995), Constraints on seismic velocities in the Earth from traveltimes, Geophys. J. Int. 122, 108-124.

Kennett, B.L.N. and Gudmundsson, O. (1996). Ellipticity corrections for seismic phases, Geophys. J. Int. 127, 40-48.

Lay, T. and Wallace, T.C. (1995). Modern global seismology, 521 pp., Academic Press.

Lee, W.H.K. and Lahr, J.C. (1975). HYPO71 (revised): A computer program for determining local earthquakes hypocentral parameters, magnitude, and first motion pattern. U.S. Geological Survey Open-File Report 75-311, 100 pp.

Lienert, B.R. and Havskov, J. (1995). A computer program for locating earthquakes both locally and globally. Seismological Research Letters 66, 26-36.

Lienert, B.R. (1997). Assessment of earthquake location accuracy and confidence region estimate using known nuclear tests. Bull. Seismol. Soc. Am. 87, 1150-1157.

Lomax, A., Virieux, J., Volant, Ph. and Gerge-Thierry, C. (2000). Probabilistic earthquake location in 3D and layered models. In: Thurber, C. H. and Rabinovitz, N. (Eds.)(2000). Advances in seismic event location. Kluwer Academic Publishers, 101-134.

Lomax, A., Zollo, A., Capuano, P. and Virieux, J. (2001). Precise, absolute earthquake locations under Somma-Vesuvius volcano using a new three-dimensional velocity model. Geophys. J. Int. 146, 313-331.

McLaren, J. P., and Frohlich, C. (1985). Model calculations of regional network locations for earthquakes in subduction zones. Bull. Seism. Soc. Am., 75, 2, 397-413.

Morelli, A., and Dziewonski, A.M. (1993), Body-wave traveltimes and a spherically symmetric P- and S-wave velocity model, Geophys. J. Int. 112, 178-194.

Müller, G. (1977). Earth flattening approximation for body waves derived from geometric ray geometry - improvements, corrections and range of applicability, J. Geophys. 42, 429-436.

Parolai, S., Trojani, L., Monachesi, G., Frapiccini, M., Cattaneo, M. and Augliera, P. (2001). Hypocenter location accuracy and seismicity distribution in the Central Apennines (Italy). Journal of Seismology 5, 243-261.

Pujol, J. (2000). Joint event location – the JHD technique and applications to data from local networks. In: Thurber Rabinovitz(2000), 163-204.

Ringdal, F. and. Kennett, B.L.N (Eds.) (2001). Special issue: Monitoring the Comprehensive Nuclear-Test-Ban Treaty: Source location. Pure appl. Geophys., 158, Number 1/2, 1-419.

Roberts, R.G., Christofferson, A. and Cassedy, F. (1989). Real time event detection, phase identification and source location using single station 3 component seismic data and a small PC. Geophysical Journal 97, 471-480.

Ružek, B. and Kvasnička, M. (2001). Differential evolution algorithm in earthquake hypocenter location. Pure appl. geophys. 158, 667-693.

Saari, J. (1991). Automated phase picker and source location algorithm for local distances using a single three-component seismic station. Tectonophysics 189, 307-315.

Sambridge, M.S. and Kennett, B.L.N. (1986). A novel method of hypocenre location. Geophys. J. R. astr. Soc., 87, 679-697.

Sambridge, M.S. and Kennett, B.L.N. (2001). Seismic event location: nonlinear inversion using a neighbourhood algorithm. Pure appl. Geophys., 158, 241-257.

Schöffel, H.-J. and Das, S. (1999). Fine details of the Wadati-Benioff zone under Indonesia and its geodynamic implications. J. Geophys. Res. 104, 13101-13114.

Shearer, P. M. (1999). Introduction to seismology, 260 pp., Cambridge University Press.

Stein, S. (1991). Introduction to seismology, earthquakes and Earth structure. Lecture notes, Department of Geological sciences, Northwestern University, USA.

Schwartz, S. Y., Dewey, J.W., and Lay, T. (1989). Influence of fault plane heterogeneity on the seismic behavior in southern Kurile Islands arc. J. Geophys. Res. 94, 5637-5649.

Schweitzer, J. (2001). HYPOSAT – An enhanced routine to locate seismic events. Pure and Applied Geophysics 158, 277-289.

Smith, G. P. and Ekström, G. (1996). Improving teleseismic event locations using a three-dimensional Earth model. Bull. Seism. Soc. Am., 86, 3, 788-796.

Spallarossa, D., Ferretti, G., Augliera, P., Bindi, D. and Cattaneo, M. (2001). Reliability of earthquake location procedures in heterogeneous areas: synthetic tests in the South Western Alps, Italy. Phys. Earth Planet. Int. 123, 247-266.

Sykes, L.R. (1966). The seismicitty and the deep structure of island arcs. J. Geophys. Res. 27, 2981-3006.

Thurber, C. H. and Rabinovitz, N. (Eds.) (2000). Advances in seismic event location. Kluwer Academic Publishers, 266 pp.

Thurber, C. H. and Engdahl, E.R. (2000). Advances in global seismic event location. In: Thurber and Rabinovitz (2000), 3-22.

Thurber, C. H. and Kissling, E. (2000). Advances in travel-time calculations for three-dimensional structures. In: Thurber and Rabinovitz (2000), 71-100.

Uhrhammer, R. A. (1980). Analysis of small seismographic station networks. Bull. Seism. Soc. Am., 70, 4, 1369-1379.

Wadati, K. (1933). On the travel time of earthquake waves. Part. II, Geophys. Mag. (Tokyo) 7, 101-111.

Waldhauser, F. and Ellsworth, W.L. (2000). A double-difference earthquake location algorithm: method and application to the Northern Hayward fault, California. Bull. Seism. Soc. Am. 90, 13553-1368.

Wiechert, E. (1907). Über Erdbebenwellen. Theoretisches über die Ausbreitung der Erdbebenwellen. Nachrichten von der Königlichen Gesellschaft der Wissenschaften zu Göttingen, Mathematisch-physikalische Klasse, 413-529.

3.4	Determination of fault-plane solutions

3.4.1	Introduction

The direction (polarity) and amplitude of motion of a seismic wave arriving at a distant station depends both on the wave type considered and the position of the station relative to the motion in the earthquake source. This is illustrated by Figs. 3.21a and b.

Fig. 3.21a represents a linear displacement of a point source S while Fig. 9b depicts a right lateral (dextral) shear dislocation along a fault plane F. Shear dislocations are the most common model to explain earthquake fault ruptures. Note that in the discussion below we consider the source to be a point source with dimension much smaller than the distance to the stations and the wave length considered. First we look into the situation depicted in Fig. 3.21a. When S moves towards (1 then this station will observe a compressional (+) P-wave arrival (i.e., the first motion is away from S), (4 will record a P-wave of opposite sign (-) , a dilatation (i.e., first motion towards S), and station (2 will receive no P-wave at all. On the other hand, S-waves, which are polarized parallel to the displacement of S and perpendicular to the direction of wave propagation, will be recorded at (2 but not at (1 and (4 while station (3 will receive both P- and S-waves.

Fig. 3.21  Direction of source displacement with respect to seismic stations (i for a) a single force at point S and b) a fault rupture F. Note that in the discussion below we consider the source to be a point source with an rupture dimension much smaller than the distance to the stations.

Somewhat different is the case of a fault rupture (Fig. 3.21b). At stations (1 and (5, which are positioned in the strike direction of the fault, the opposite signs of P motion on both side of the fault will cancel, i.e., no P-waves will be observed. The latter also applies for station (3 which is sited perpendicular to the fault. On the other hand, stations (2 and (4, which are positioned at an angle of 45° with respect to the fault, will record the P-wave motions with maximum amplitudes but opposite sign. This becomes clear also from Fig. 3.23a. It shows the different polarities and the amplitude "lobes" in the four quadrants. The length of the displacement arrows is proportional to the P-wave amplitudes observed in different directions from the fault. Accordingly, by observing the sense of first motions of P-waves at many stations at different azimuths with respect to the source it will be possible to deduce a "fault-plane solution". But because of the symmetry of the first-motion patterns, two potential rupture planes, perpendicular to each other, can be constructed. Thus, on the basis of polarity data alone, an ambiguity will remain as to which one was the acting fault plane. This can only be decided by taking into account additional data on azimuthal amplitude and frequency or wave-form patterns, which are controlled by the Doppler effect of the moving source, and/or field data on the orientation and nature of seismotectonic faults.

In accordance with the above, the amplitude distribution of P waves for a point source with pure double-couple shear mechanism is described in a spherical co-ordinate system ((, () (Aki an Richards, 1980; see Fig. 3.22) by

AP ((, () = cos ( sin 2(.				           (3.67)

This expression divides the focal sphere into 4 quadrants. The focal sphere for a seismic point source is a conceived sphere of arbitrarily small radius centered on the source. Within each quadrant the sign of the P-wave first motion (polarity) does not change but amplitudes are large in the center of the quadrant and small (or zero) near to (or at) the fault plane and the auxiliary plane. The nodal lines for P-waves, on which AP ((, () = cos ( sin 2( = 0, separate

the quadrants. They coincide with the horizontal projection of the two orthogonal fault planes traces through the focal sphere. Opposite quadrants have the same polarity, neighboring quadrants different polarities. Note that compression is observed at stations falling in the tension quadrant (force directed away from the point source) while dilatation is observed at stations falling in the compression quadrant (force directed towards the point source).

Fig. 3.22  Map view of P-wave radiation pattern for a shear fault. ( is the azimuth in the plane while ( is in fact three-dimensional. See also Fig. 3.23.Black areas: polarity +, white areas - .

The position of the quadrants on the focal sphere depends on the orientation of the active fault and of the slip direction in space. This is illustrated by Fig. 3.23. which shows the P-wave radiation pattern for a thrust event with some strike-slip component. Thus, the estimation of the P-wave first motion polarities and their back-projection onto the focal sphere allows us to identify the type of focal mechanism of a shear event (fault-plane solution). The only problem is, that the hypocenter and the seismic ray path from the source to the individual stations must be known. This may be difficult for a heterogeneous model with 2D or 3D-velocity structure.

Fig. 3.23  Radiation pattern of the radial displacement component (P-wave) due to a double-couple source: a) for a plane of constant azimuth (with lobe amplitudes proportional to sin2() and b) over a sphere centered on the origin. Plus and minus signs of various sizes denote amplitude variation (with ( and () of outward and inward directed motions. The fault plane and auxiliary plane are nodal lines on which cos( sin2( = 0. The pair of arrows in a) at the center denotes the shear dislocation. Note the alternating quadrants of inward and outward directions. (Modified from Aki and Richards 1980 ; with kind permission of the authors).

Fault-plane solutions based on P-wave first motion polarities will be better constrained if additionally the different radiation pattern of S-waves displacement amplitudes is taken into account. An example is given in Fig. 3.24 for the same fault-plane solution as shown in Fig. 3.23 for P-waves.

Fig. 3.24  Radiation pattern of the transverse displacement component (S-wave) due to a double-couple source. a) in the plane (( = 0, ( = (( and b) over a sphere centered on the origin. Arrows imposed on each lobe in a) show the direction of particle displacement associated with the lobe while the arrows with varying size and direction in the spherical surface in b) indicate the variation of the transverse motions with ( and (. There are no nodal lines as in Fig. 3.23 but only nodal points where there is zero motion. Note that the nodal point for transverse motion at ((, () = (45°, 0°) at T is a maximum in the pattern for longitudinal motion (see Fig.3.23) while the maximum transverse motion (e.g., at ( = 0) occurs on a nodal line for the longitudinal motion. The pair of arrows in a) at the center denotes the shear dislocation. (Modified from Aki and Richards 1980; with kind permission of the authors).

In the case of a double-couple mechanism, according to Fig. 3.22, the S-wave amplitude pattern follows the relationship (see Aki and Richards, 1980)

AS = cos2( cos(( - cos( sin((			           (3.68)

with ( and ( - unit vectors in ( and ( direction, AS - shear-wave displacement vector.

3.4.2	Manual determination of fault-plane solutions

Manual fault-plane solutions are normally based on P-wave polarity readings only which are plotted on two kinds of projections, either the equal-angle Wulff net or the Lambert-Schmidt equal area projection (Figs. 3.25a and b; see also Aki and Richards, 1980, Vol. 1, p. 109-110).

The latter provides a less cluttered plot of data with take-off angles less than 45° but in principle the procedure of constructing the fault planes is the same (see WS 3.2 and WS 3.3).

# Fig. 3.25a  The equal angle Wulff net.

# Fig. 3.25b  The equal area Lambert-Schmidt net.

To obtain a fault-plane solution basically three steps are required:

- Calculating the positions of the penetration points of the seismic rays through the focal sphere which are defined by the ray azimuth AZM and the take-off angle AIN of the ray from the source.

- Marking these penetration points through the upper or lower hemisphere in a horizontal projection of that sphere using different symbols for compressional and dilatational first arrivals. Usually, lower hemisphere projections are used. Rays which have left the upper hemisphere have to be transformed into their equivalent lower hemisphere ray. This is possible because of spherical symmetry of the radiation pattern (see Figs. 3.26 and 3.27).

- Partitioning the projection of the lower focal sphere by two perpendicular great circles which separate all (or at least most) of the + and - arrivals in different quadrants.

Fig. 3.26  Transformation of a ray leaving the focal sphere upwards into an equivalent downward ray with same polarity and changed incidence angle and azimuth.

Fig. 3.27  (below): Two rays, leaving the focal sphere in opposite directions, reach - because of the symmetry of radiation pattern - the stations 1 and 2 with the same polarity. The crossing point of the up-going ray with the focal sphere can, therefore, be remapped according to the formulae given in Fig. 3.26 into a crossing point with the lower hemisphere which coincides with the ray crossing-point for station 2.

Fig. 3.28 shows the angles which describe the orientation and motion of a fault plane and Fig. 3.29 shows their determination in the net projections. The strike angle ( is measured clockwise against North ( 0° ( ( ( 360° ). To resolve the 180° ambiguity, it is assumed that when looking into the strike direction the fault dips to the right hand side (i.e., its fault-trace projection is towards the right of the net center). The dip angle ( describes the inclination of the hanging wall against the horizontal ( 0° ( ( ( 90° ). The rake angle ( describes the displacement of the hanging wall relative to the foot wall ( -180° ( ( ( 180° ). ( = 0 corresponds to slip in strike direction, ( > 0 means upward motion of the hanging wall (i.e., reverse or thrust faulting component) and ( < 0 downward motion (i.e., normal faulting component).

# Fig. 3.28  Angles describing the orientation and motion of faults (see text).

In Fig. 3.29 P1, P2 and P3 mark the positions of the poles of the planes FP1 (fault plane), FP2 (auxiliary plane) and EP (equatorial plane) in their net projections. From Fig. 3.28 it is obvious that all three planes are perpendicular to each other (i.e., 90o apart) and intersect in the poles of the respective third plane, i.e., FP1 and FP2 in P3, FP1 and EP in P2 etc. Note that on the basis of polarity readings alone it can not be decided whether FP1 or FP2 was the active fault. Discrimination from seismological data alone is still possible by requires additional study of the directivity effects such as azimuthal variation of frequency (Doppler effect), amplitudes and/or waveforms. For sufficiently large shocks these effects can more easily be studied in low-frequency teleseismic recordings while in the local distance range high-frequency waveforms and amplitudes may be strongly influenced by resonance effects due to low-velocity near-surface layers. Seismotectonic considerations or field evidence from surface rupture in case of strong shallow earthquakes may allow us to resolve this ambiguity, too. Figs. 3.30 and 3.31 depict several basic types of earthquake faulting and their related fault-plane solutions in so-called "beach-ball" presentations of the net projections.

Fig. 3.29  Determination of the fault plane parameters (, ( and ( in the net diagrams. The polarity distribution, slip direction and projection of FP1 shown qualitatively correspond to the faulting case depicted in Fig. 3.28. For abbreviations used see text. Note: (* = 180° - ( when the center of the net lies in the tension (+) quadrant (i.e., event with thrust component) or (* = -( when the center of the net lies in the pressure quadrant (i.e., event with normal faulting component.

# Fig. 3.30  Basic types of earthquake faulting for some selected dip and rake angles. Note that

mixed types of faulting occur when ( ( 0, 180o or ( 90o., e.g., normal faulting with strike-slip component or strike-slip with thrust component. Also, dip angles may vary between 0o < ( ( 90o. For fault plane traces and polarity distributions of these faulting types in their "beach-ball presentation" see Fig. 3.31.

Fig. 3.31  Beach-ball presentation of the net projections of the fault plane cut-traces and of the penetration points of the T-and P-axes through the lower focal hemisphere for different faulting mechanisms. White sectors correspond to negative and black sectors to positive first-motion polarities.

3.4.3	Accuracy of fault-plane solutions

Fault planes determined by eye-fit to the polarity data may be uncertain by about ( 10o. This is acceptable. Even computer assisted best fits to the data will produce different acceptable solutions within about the same error range with only slightly different standard deviations (see, e.g., Fig. 1 in WS 3.3, NEIC and HRVD solutions, respectively).

In addition, one has to be aware that different fitting algorithm or error-minimization procedures may produce different results within this range of uncertainty for the same data. A poor distribution of seismograph stations (resulting in insufficient polarity data for the net diagram), erroneous polarity readings and differences in model assumptions (e.g., in the velocity models used) may result in still larger deviations between the model solution and the actual fault planes. One should also be aware that the assumed constant angular (45o) relationship between the fault plane on the one hand and the pressure and tension axis on the other hand is true in fact only in the case of a fresh rupture in a homogeneous isotropic medium. It may not be correct in the stress environment of real tectonic situations (i.e., P and T ( (1 and -(3, respectively; see discussion in sub-section 3.1.2.4).

| Topic | Determination of fault plane solutions |
| --- | --- |
| Authors | Michael Baumbach, and Peter Bormann, Geoforschungszentrum Potsdam, Division 2: Solid Earth Physics and Disaster Research, Telegrafenberg, D-14473 Potsdam, Germany, Fax: +49 331 288 1204; E-mail: baum@gfz-potsdam.de |
| Version | September 1999 |

# 1  Aim

The exercise aims at:

- 	Understanding how fault slip affects the polarities of P-waves;

- 	Understanding the presentation of P-wave polarities in an equal angle (Wulff net) or equal area projection (Lambert-Schmidt net) of the focal sphere;

- Constructing a fault-plane solution and the related parameters (P- and T-axes, displacement vector) for a real earthquake;

- Relating the fault-plane solution to the tectonic setting of the epicentral area.

2  Data and procedures

Before a fault-plane solution for a teleseismic event can be constructed, the following steps must be completed:

- Interpretation of P-wave first-motion polarities from seismograms at several stations;

- Calculation of epicentral distances and source-to-station azimuths for these stations;

- Calculation of the take-off angles for the seismic P-wave rays leaving the hypocenter towards these stations. This requires the knowledge of the focal depth and of the P-wave velocity at this depth (see EX 3.3).

For the calculations b) and c) standard Earth velocity models are used (e.g., Kennett, 1991).

In the case of local events it is necessary to determine which branch of the travel-time curve is arriving first. The events should be located, if possible, with a special layered crustal velocity model for that region. Most such programs provide both the source-station azimuths and take-off angles in their output files.

The exercise below is based on the definitions, relationships and diagrams (Figs. 3.27 – 3.33) given in the NMSOP, Chapter 3, section 3.4.2 “Manual determination of fault plane solutions.”. As an example consider the data in Table 1 that was determined following steps a)-c), by using the program HYPO71, for a locally recorded aftershock of the Erzincan earthquake in Turkey (Date: 12.04.1992, Ml = 2.8 , latitude = 39.519° N, longitude = 39.874° E, source depth h = 3 km; station distance up to 50 km).

Note: The take-off angles, AIN, calculated for a ray arriving at a given seismic station may vary significantly depending on the assumed velocity model in the source region. Also, for an average single layer crustal model of 30 to 40 km thickness, all P-wave first arrivals within a distance of about 120 - < 200 km are Pg and up-going. That is, they emerge only from the upper half of the focal hemisphere. Also, when using HYPO71 with the average global two-layer crust according to the velocity model IASP91 (Kenneth 1991) only upper hemisphere take-off angles would have been calculated for the first P-wave arrivals up to distances of 50 km. But in the epicentral area under consideration a significant velocity increase in the upper crust was already found at 4 km depth (increase of vp =  5.3 km/s to 6.0 km/s). Accordingly, stations up to 50 km distance were reached by upper or lower focal sphere rays (see Fig. 3.29). Since only lower hemisphere projections will be used in the exercise values, for upper hemisphere rays (AIN > 90°) must be corrected according to Fig. 3.28. Conclusion: AIN calculations based on strongly biased velocity models might result in inconsistent fault-plane solutions or not permit a proper separation of polarity readings into quadrants at all!

Table 1 gives the needed primary data. They were taken from the output file of the program HYPO71 with which the event was located. The first five columns of this file contain, as an example for the two stations ALI and ESK in Tab. 1, the following data:

STN	DIST	AZM	AIN	PRMK

ALI	  3.7	  40	130	IPD0

ESK	22.7	312	62	IPU1

with STN - station code; DIST - epicentral distance in km; AZM - azimuth towards the station clockwise in degree from north; AIN - take-off angle of the ray towards the station, measured as in Fig. 3.28, and calculated for the given structure-velocity model; PRMK - P-wave reading remarks. In the column PRMK  P stands for P-wave onset, I for impulsive (sharp) or E for emergent (less clear) onset, D for clear (or - for poor) dilatational (downward) first motion, U for clear (or + for poor) compressional (upward) first motion as read at the station. The last character may range between 0 and 4 and is a measure of the quality (clarity) of the onset and thus of the weight given to the reading in the calculation procedure, e.g., 4 for zero and 0 for full weight. In case of the above two stations the values for ALI would need to be corrected to get the respective values for the equivalent lower hemisphere ray, i.e., AINc = 180° - 130° = 50° and AZMc = 180° + 40° = 220° while the values for ESK can be taken unchanged from the HYPO71 output file.

# 3  Tasks

Task 1:

If in Table 1 AIN > 90°, then correct take-off angles and azimuths for lower hemisphere projection: 	AINc = 180° - AIN,  AZMc = AZM(<180°) + 180° or AZM((180°) - 180°. In case of AIN < 90° the original values remain unchanged.

Task 2:

Place tracing paper or a transparency sheet over the Wulff or Lambert-Schmidt net projection (see Fig. 3.27a or b in 3.4.2). Mark on it the center and perimeter of the net as well as the N, E, S and W directions. Pin the marked sheet center with a needle to the center of the net.

Task 3:

Mark the azimuth of the station on the perimeter of the transparency and rotate the latter until the tick mark is aligned along an azimuth of 0°, 90°, 180° or 270°. Measure the take-off angle from the center of the net along this azimuth. This gives the intersection point of the particular P-wave ray with the lower hemisphere. Mark on this position the P-wave polarity with a neat + for compression or ( for dilatation (U or D in Tab. 1) using different colors for better distinction of closely spaced polarities of different sign. Note: The proper distance (d) of the polarity entry from the center of the net corresponds to d = r ( tan( AIN / 2) for the Wulff net and d = r ( sin( AIN / 2) for the Lambert-Schmidt net with r the radius of the given net. In case that rays left the source through the upper hemisphere (AIN > 90°) AINc for lower hemisphere projection has to be calculated and used!

Table 1  Original and corrected values of ray azimuth (AZM and AZMc) and take-off angles (AIN and AINc) towards stations of a temporary network which recorded the Erzincan aftershock of April 12, 1994. POL - polarity of P-wave first motions.

| STA | AZM (degree) | AIN (degree) | POL | AZMc (degree) | AINc (degree) |
| --- | --- | --- | --- | --- | --- |
| ALI ME2 KAN YAR ERD DEM GIR UNK SAN PEL GUN ESK SOT BA2 MOL YUL ALT GUM GU2 BAS BIN HAR KIZ AKS SUT | 40 134 197 48 313 330 301 336 76 327 290 312 318 79 297 67 59 320 320 308 295 24 311 284 295 | 130 114 112 111 103 102 102 101 62 62 62 62 62 62 62 62 62 62 62 62 62 62 62 62 62 | D D D D D D U D U D U U D U U U D U D D U D U D U |  |  |

Task 4:

By rotating the transparent sheet with the plotted data over the net try to find a great circle which separates as good as possible the expected quadrants with different first motion signs. This great circle represents the intersection trace of one of the possible fault (or nodal) planes (FP1) with the lower half of the focal sphere. Note 1: All N-S connecting lines on both nets are great circles! Note 2: Inconsistent polarities that are close to each other may be due to uncertainty in reading relatively small P-wave amplitudes. The phenomemon occurs particularly for takeoff angles near nodal (fault) planes. Thus, clusters of inconsistent polarities may guide you in finding the best separating great circle. However, be aware that isolated inconsistent polarities might be due to false polarity switching or erroneous first motion polarity reading at the seismic station.

Task 5:

Mark point A at the middle of FP1 and find, on the great circle perpendicular to it, the pole P1 of FP1, 90o apart (see Fig. 3.31). All great circles, passing this pole are perpendicular to the FP1. Since the second possible fault plane (FP2) must be perpendicular to the FP1, it has to pass P1. Find, accordingly, FP2 which again has to separate areas of different polarity.

Task 6:

Find the pole P2 for FP2 (which is on FP1!) and delineate the equatorial plane EP. The latter is perpendicular to both FP1 and FP2, i.e., a great circle through the poles P1 and P2. The intersection point of FP1 and FP2 is the pole of the equatorial plane (P3).

Task 7:

Mark the position of the pressure and tension axes on the equatorial plane and indicate their direction towards (P) and from the center (T) of the considered net (see Fig. 3.31). Their positions on the equatorial plane lie in the center of the respective dilatational (- for P) or compressional (+ for T) quadrant, i.e., 45° away from the intersection points of the two fault planes with the equatorial plane. Note:

All angles in the net projections have to be measured along great circles!

Task 8:

Mark the slip vectors, connecting the intersection points of the fault planes with the equatorial plane, with the center of the considered net If the center lies in a tension quadrant, then the slip vectors point to the net center (see Fig. 3.31). If it lies in a pressure quadrant, then the slip vector points in the opposite direction. The slip vector shows the direction of displacement of the hanging wall.

Task 9:

Determine the azimuth (strike direction () of both FP1 and FP2. It is the angle measured clockwise against North between the directional vector connecting the center of the net with the end point of the respective projected fault trace lying towards the right of the net center (i.e., with the fault plane dipping towards the right; see Fig. 3.31).

Task 10:

Determine the dip angle ( (measured from horizontal) for both FP1 and FP2 by putting their projected traces on a great circle. Measure  (  as the difference angle from the outermost great circle towards the considered fault plane trace.

Task 11:

Determine the slip direction (i.e., the sense of motion along the two possible fault planes. It is obtained by drawing one vector each from the center of the net to the poles P1 and P2 of the nodal planes (or vice versa from the poles to the center depending on the sign of the rake angle (). The vector from (or to) the center to (or from) P1 (P2) shows the slip direction along FP2 (FP1).The rake angle  (  is positive in case the center of the net lies in the tension (+) quadrant (i. e. an event with a thrust component) and negative when it lies in the pressure (-) quadrant (event with a normal faulting component). In the first case ( is 180° - (*.  (* has to be measured on the great circle of the respective fault plane between its crossing point with the equatorial plain and the respective azimuth direction of the considered fault plane (see Fig. 3.31). In the second case ( = - (*. For a pure strike slip motion (( = 90° ) ( = 0 defines a left lateral strike-slip and  ( = 180° defines a right-lateral strike-slip.

Task 12:

The azimuth of the pressure and the tension axes, respectively, is equal to the azimuth of the line connecting the center of the net through the P and T point with the perimeter of the net. Their plunge is the dip angle of these vectors against the horizontal (to be measured as for ().

Task 13:

Estimate the parameters of the fault planes and of the stress axes for the Erzincan aftershock and insert your results into Table 2 below:

#### Table 2

strike			dip		    rake

Fault plane  1

Fault plane  2

azimuth	                  plunge

Pressure axis

Tension axis

Note: The angles may range between:

0°  <   strike   <  360°               0°  <  incidence angle  <  180°

0°  < azimuth <  360°

0°  <     dip    <     90°

0° <   plunge  <     90°

-180° <      rake   <   180°

Task 14:

The question of which of the nodal planes was the active fault plane, and hence the other was the auxiliary plane, cannot be answered on the basis of the fault-plane solution alone. Considering the event in its seismotectonic context may give an answer. Therefore, we have marked the epicenter of the event in Figure 1 with an open star at the secondary fault F2.

- Decide which was the likely fault plane (FP1 or FP2)?

- What was the type of faulting?

- What was the direction of slip? and

- Is your solution compatible with the general sense of plate motion in the area as well with the orientation of the acting fault and the orientation of stress/deformation in the area? (Yes or No)?

Figure 1  Epicenters of aftershocks between March 21 and June 16, 1992 of the March 13, 1992 Erzincan earthquake, Turkey. The open circles represent the main shock and its strongest aftershock on March 15, and the open star the analyzed aftershock. F1, F2 and F3 are secondary faults to the North Anatolian Fault (NAF). Black arrows - directions of relative plate motion, open arrows - direction of maximum horizontal compression as derived from centroid moment tensor solutions of stronger earthquakes (courtesy of H. Grosser).

4  Solutions

In the Table 3 below the authors have given the data for their own  freehand fits  together with the values for the best PC fit to the data (in brackets). If your manually determined results differ by more than about 20o or even show a different type of faulting mechanism, you should critically check your data entries and/or fault-plane fits again.

### Table 3

strike			dip			rake

Fault plane  1 (FP1)	       280o (278.5°)	       40o (39.9°)	  68o (67.4°)

Fault plane  2 (FP2)	       130o (127.0o)	      54o	(53.7o)	           108o (107.8o)

azimuth	                  plunge

Pressure axis	                  205o (204.4o)	       7o (7.1o)

Tension axis		        90o (88.6o)	     73o (74.0o)

The answers to the questions in Task 14 are:

- FP2 was more likely the active fault.

- The aftershock was a thrust event with a very small right-lateral strike-slip component.

- The slip direction is here strike - rake azimuth, i.e., for FP2 130° - 108° = 12° from north. This is close to the direction of maximum horizontal compression (15°) in the nearby area as derived from centroid moment tensor solutions of stronger events.

- The strike of FP2 for this event agrees with the general direction of mapped surface fault strike and is consistent with the tendency of plate motion direction in the area under study. Therefore, it is highly probable that FP2 was the acting fault.

| Topic | Determination of source parameters from seismic spectra |
| --- | --- |
| Authors | Michael Baumbach, and Peter Bormann, Geoforschungszentrum Potsdam, Division 2: Solid Earth Physics and Disaster Research, Telegrafenberg, D-14473 Potsdam, Germany, Fax: +49 331 288 1204; E-mail: baum@gfz-potsdam.de |
| Version | September 1999 |

1  Aim

This exercise shows how to estimate the source parameters seismic moment, size of the rupture plane, source dislocation and stress drop from data in the frequency domain only and how the results depend on the underlying model assumptions. These parameters could also be estimated in the time domain. However, for estimation in the time domain the records have to be converted into true ground motion (displacement) records. This may be a problem if the bandwidth of the recording system is limited (e.g., short-period records) or if the phase response of the system is not well known. For estimation in the frequency domain only the amplitude response of the instrument is needed.

2  Data

Figure 1 shows a velocity record (vertical component) of an aftershock of the 1992 Erzincan earthquake (Turkey). Figure 2 shows the corresponding displacement spectrum of the P-wave. The calculated spectrum was corrected for the amplitude response of the recording system (which includes both response of the velocity seismometer and the anti-aliasing filter of the recorder). Furthermore, the P-wave spectrum was corrected for attenuation, exp(i(t/2Qp ). Qp had been estimated beforehand from coda Qc- observations in the area under study assuming that Qp = 2.25 Qc. This is a good approximation under the assumption that vp/vs = 1.73, Qc = Qs and the pure compressional Q( (( - bulk modulus) is very large (( (). In Figure 2 also the noise spectrum, treated in the same way as the P-wave spectrum, was computed and plotted in order to select the suitable frequency range for analysis (with signal-to-noise ratio SNR > 3).

At low frequencies typical P- and S-wave spectra approach a constant amplitude level uo and at high frequencies the spectra show a decay that falls off as f -2  to f -3. Plotted on a log-log scale the spectrum can be approximated by two straight lines. The intersection point is the corner frequency fc. uo and fc are the basic spectral data from which the source parameters will be estimated. Event and material data required for further calculations are the epicentral distance (, the source depth h, the  rock density (, the P-wave velocity vP, and the averaged radiation pattern ( for P-waves. Respective values are given under 3.1 below. Other needed parameters can then be calculated.

Note: The apparent increase of spectral amplitudes in Figure 2 for f > 35 Hz is not real but due to antialiasing filtering of the record. Thus, this increase should not be considered in the following analysis.

Figure 1  Record of an Erzincan aftershock (vertical component). For the indicated P-wave window the displacement spectrum shown in Figure 2 has been calculated.

Figure 2  P-wave (upper curve) and noise spectrum (lower curve) of the record shown in Figure 1, corrected for the instrument response and attenuation.

3  Procedures

The parameters to be estimated are:

-   Seismic moment    			Mo  = ((D A    					    (1)

(with ( - shear modulus; (D - average source dislocation, and  A - size of the rupture plane)

-   Source dislocation (D

-   Source dimension (radius R and area A)

-   Stress drop ((

The following relationships hold:

3.1  Seismic moment Mo

Under the assumption of a homogeneous Earth model and constant P-wave velocity  vp, the seismic moment M0  can be determined from the relationship:

M0  =  4  (  r vp3  (  uo  /  ( (  Sa )					    (2)

In the case with:				density			  (  =  2.7 g/cm3

P-wave velocity	 vp  =  6 km/sec

source depth		  h  =  11.3 km

epicentral distance	 (  =  18.0 km

hypocentral distance	  r  =  ( ( h2 + (2 ) 							(travel path)

incidence angle	  i  =  arc cos ( h / r )

free surface amplification  Sa  for P-waves

averaged radiation pattern (  =  0.64 for P-waves.

Note the differences in dimensions used! M0 has to be expressed in the unit  Nm = kg m2 s-2. Sa can be determined by linear interpolation between the values given in Table 1. They were computed for the above given constant values of vp and ( (homogeneous model) and assuming a  ratio vp/vs = 1.73.  i is the angle of incidence, measured from the vertical.

Table 1  Surface amplification Sa for P-waves; i  is the incidence angle.

| i | Sa | i | Sa | i | Sa |
| --- | --- | --- | --- | --- | --- |
| 0 5 10 15 20 25 | 2.00 1.99 1.96 1.92 1.86 1.79 | 30 35 40 45 50 55 | 1.70 1.60 1.49 1.38 1.26 1.14 | 60 65 70 75 80 85 | 1.02 0.90 0.79 0.67 0.54 0.35 |

3.2  Size of the rupture plane

For estimating the size of the rupture plane and the source dislocation one has to adopt a kinematic (geometrical) model, describing the rupture propagation and the geometrical shape of the rupture area. In this exercise computations are made for three different circular models (see Table 2), which differ in the source time function and the crack velocity vcr. vs is the S-wave velocity, which is commonly assumed to be vs = vp / (3.

Table 2  Parameters of some commonly used kinematic rupture models.

| 1. Brune (1970) | vcr = 0.9 Vs | Kp = 3.36 | Ks =2.34 |
| --- | --- | --- | --- |
| 2. Madariaga I (1976) | vcr = 0.6 Vs | Kp = 1.88 | Ks = 1.32 |
| 3. Madariaga II (1976) | vcr = 0.9 Vs | Kp = 2.07 | Ks = 1.38 |

The source radius R (in m) can then be computed from the relationship

R  =  vs  Kp/s  /  2( fcp/s					    (3)

with vs – shear-wave velocity in km/s, fcp/s - corner frequency of the P- or S-waves, respectively, in Hz and Kp and Ks being the related model constants and vs. The differences in Kp and Ks between the various models are due to different assumptions with respect to crack velocity and the rise time of the source-time function. Only Kp has to be used in the exercise (P-wave record!). The size of the circular rupture plane is then

A = ( R2. 							    (4)

3.3  Average source dislocation (D

According to (1) the average source dislocation is

(D = M0/ ((A ).						    (5)

Assuming vs = vp/1.73 it can be computed knowing M0, the source area A and the shear modulus ( = vs2 (.

3.4  Stress drop

The static stress drop (( describes the difference in shear stress on the fault plane before and after the slip. According to Keilis Borok (1959) the following relationship holds for a circular crack with a homogeneous stress drop:

(( = 7 M0/ (16 R3).						    (6)

The stress drop is expressed in the unit of Pascal,   Pa = N m-2 = kg m-1 s-2 = 10-5 bar.

4  Tasks

Task 1:

Select in Figure 2 the frequency range f1 to f2 that can be used for analysis (SNR > 3):

f 1  = ............... Hz			f 2  = ............... Hz

Task 2:

Estimate the low-frequency level, uo , of the spectrum by approximating it with a 	horizontal line. Note in Figure 2 the logarithmic scales and that the ordinate dimension is nm s = 10-9m s.

uo  = .................... m s

Task 3:

Estimate the exponent, n, of the high frequency decay, f -n ; mark it by an inclined straight line.

n = ..........

Task 4:

Estimate the corner frequency, fcp  (the intersection between the two drawn straight lines).

fcp = ............... Hz

Task 5:

Calculate from the given event parameters and relationships given in 3.1 and Table 1 the values for:

r = ………km			i =……….°		Sa = ……….		Mo = …………Nm.

Task 6:

Using the equations (3), (4), (5) and (6) calculate for the three circular source models given in Table 2 the parameters

- source radius R and  source area A,

- shear modulus ( and average displacement (D and

- stress drop ((.

Write the respective values in Table 3

#### Table 3

| Model | R (m( | A (m2( | (D (m( | (( (MPa( |
| --- | --- | --- | --- | --- |
| 1. Brune |  |  |  |  |
| 2. Madariaga I |  |  |  |  |
| 3. Madariaga II |  |  |  |  |

Note:  Since (( ( R-3 the estimate of stress drop very much depends on fc, a parameter which can not be estimated very precisely from real spectral data. In the case of non-circular, e.g., rectangular fault ruptures, two corner frequencies may exist which are controlled by the width W and the length L of the rupture plane. In addition, differences in the assumed mode of crack propagation (e.g., unilateral, bilateral, or radial) and the velocity of crack propagation, vcr, influence the parameters calculated from spectral data (see Information Sheet IS 3.1). Accordingly, stress drop values may be, in the worst case, uncertain up to about two orders of magnitude. Therefore, in studying possible systematic differences in source parameters derived from spectral data for events in a given area one should always stick to using one type of model. However, one must be reasonably sure about the validity of assuming that the events have similar modes of faulting and crack propagation.

5  Solutions

Although individual visual parameter readings from Figure 2 might be subjective, they should not differ by more than about  ( 10% from the values given here for tasks 1 to 5 but may be larger for 6. Acceptable average values for the read and calculated parameters are for:

Task 1:	f1 = 2 Hz, 	f2 = 30 Hz

Task2:		uo = 3 ( 10-7 m s

Task 3:	n = 3

Task 4:	fcp = 14.4 Hz

Task 5:	r = 21.3 km	i = 58o, 	Sa = 1.07, 	Mo = 6.8 ( 1013 N m

Task 6:

a)	R1 = 129 m, 		A1 = 5.23 ( 104 m2

R2 =  72 m, 		A2 = 1.63 ( 104 m2

R3 =  79 m, 		A3 = 1.96 ( 104 m2

b) 	( = 3.24 ( 1010 kg m-1 s-2		D1 = 4.0 ( 10-2 m

D2 = 1.3 ( 10-1 m

D3 = 1.1 ( 10-1 m

c)	((1 = 13.8 MPa

((2 = 79.7 MPa

((3 = 60.3 Mpa

### References

Brune, J. N. (1970). Tectonic stress and the spectra of shear waves from earthquakes. J. Geophys. Res., 75, 4997-5009.

Keilis Borok, V. I. (1959). On the estimation of the displacement in an earthquake source and of source dimensions. Ann. Geofis. 19, 205-214.

Madariaga, R. (1976). Dynamics of an expanding circular fault. Bull. Seismol. Soc. Am., 66, 639-666.

# Text boxes

AIN = 90°

AIN = 0°

fault motion

P-wave

(



Pressure axis

Tension axis

AIN = 180°

lower hemisphere

P

P: AIN, AZM

P:  AINC = 180° - AIN

AZMC = AZM ( 180°

AIN = 90o

Station 1                                                                      Station 2

V2      V1 < V2                      Velocity boundary

V1

0°

N

# Strike 

Direction of motion of the hanging wall

+180°

-180°

0°

Dip 

# Rake (

0°

## Hanging wall

Foot wall

*

i

r

Source

Epicentre

Station

i

h

(